Quotation for HZS60 Concrete batching plant (60m3/hr)

HZS60 concrete mixing plant technical parameter

| Models Items | HZS60 |
| --- | --- |
| Theory Productivity (m3/h) | 60 |
| Main Mixer | JS1000 |
| Aggregate Measuring Scope (kg) | 0-2000 |
| Aggregate Measuring Accuracy | ±2% |
| Cement Measuring Scope (kg) | 0-600 |
| Cement Measuring Accuracy | ±1% |
| Coal Ash Measuring Scope (kg) | 0-200 |
| Coal Ash Measuring Accuracy | ±1% |
| Water Measuring Scope (kg) | 0-200 |
| Water Measuring Accuracy | ±1% |
| Admixture Measuring Scope (kg) | 0-30 |
| Admixture Measuring Accuracy | ±1% |
| Power (kw) | 146 |
| Whole-Weight (kg) | 30000 |
| Aggregate Category | 3-4 |
| Quantity of Cement Silo | 2-4 |

HZS60 Concrete Mixing Plant Constitution

| No. | Item name |
| --- | --- |
| 1 | Aggregate batching system | Storage silo |
|  |  | Frame |
|  |  | Weighting hopper |
|  |  | Sensor |
|  |  | Vibrator |
|  |  | Cylinder |
|  |  | Diad |
|  |  | Electric pulley |
|  |  | Belt |
|  |  | Trough roller |
|  |  | Flat roller |
|  |  | Belt frame |
|  |  | Reverse pulley |
|  |  | Sweeper |
| 2 | Mixer system | Mixer |
|  |  | Reducer |
|  |  | Cylinder |
|  |  | Solenoid valve |
|  |  | Magnet switch |
|  |  | Electric lubricant pump |
| 3 | Slant belt | Frame |
|  |  | Electric pulley |
|  |  | Belt |
|  |  | Trough roller |
|  |  | Flat roller |
|  |  | Roller group |
|  |  | Reverse pulley |
|  |  | Sweeper |
|  |  | Walking plat |
|  |  | Feeding channel |
|  |  | Cover |
| 4 | Main frame | Upper chassis |
|  |  | Down chassis |
|  |  | Walking plat |
|  |  | Upright, inclined strut |
|  |  | Ladder |
|  |  | Support legs |
|  |  | Collect hopper |
| 5 | Water system | Water pump |
|  |  | Butterfly valve |
|  |  | Solenoid valve |
|  |  | Pipes |
|  |  | Attachment |
| 6 | Additive system | Storage tank |
|  |  | Additive pump |
|  |  | Pipes |
|  |  | Accessories |
| 7 | Air circuit system | Air compressor |
|  |  | Diad |
|  |  | Main pipe line |
|  |  | Air pipe |
|  |  | Accessories |
| 8 | Measuring system | Support |
|  |  | Solenoid valve |
|  |  | Aggregate middle hopper |
|  |  | Cylinder |
|  |  | Magnet switch |
|  |  | Cement hopper |
|  |  | Sensor |
|  |  | Butterfly valve |
|  |  | Vibrator |
|  |  | Fly coal ash hopper |
|  |  | Sensor |
|  |  | Butterfly valve |
|  |  | Vibrator |
|  |  | Water hopper |
|  |  | Sensor |
|  |  | Water discharge pump |
|  |  | Additive hopper |
|  |  | sensor |
|  |  | Butterfly valve |
| 9 | Dust remove system | Dust remove pipe line |
|  |  | Axial flow fan |
| 10 | Outside decoration | Frame |
|  |  | Color steel board |
|  |  | Door |
|  |  | Window |
| 11 | Electric control system | Control room |
|  |  | Power cabinet |
|  |  | Operating table |
|  |  | Control computer |
|  |  | LCD Controllers |
|  |  | Management software |
|  |  | IPC |
|  |  | LCD |
|  |  | Printer |
|  |  | UPS power |
|  |  | Electric components |
|  |  | AC |
|  |  | Swivel chair |
| 12 | Monitoring system | The night vision camera |
|  |  | Four image segmentation |
|  |  | Monitor |
|  |  | Power |
|  |  | Aluminium alloy cover |
|  |  | Camera support |
|  |  | Video wire |
|  |  | Electric wire |
| 13 | Dismantle type cement silo |
|  | Dismantle type cement silo |
| 14 | Screw conveyor |
|  | Screw conveyor |

TERMS AND CONDITIONS

- Price:

| S/N | Name | Specification | Unit price （CIF Argel） | Quantity | Price （CIF Argel） |
| --- | --- | --- | --- | --- | --- |
| 1 | Concrete batching plant | HZS60 | USD 112000 | One set | USD 112000 |
| 2 | Dismantled type cement silo | 100T | USD 12780 | 2 sets | USD 25560 |
| 3 | Dismantled type cement silo | 50T | USD 10400 | 2 sets | USD 20800 |
| 4 | Srew conveyor | ￠219X9m | USD 2450 | 2 sets | USD 4900 |
| 5 | Screw conveyor | ￠273X9m | USD 3300 | 2 sets | USD 6600 |

- Payment Term: 30% by T/T as advance payment, 70% by T/T 7 days before delivery goods;

- Delivery Time (not include shipping time): 35 working days after getting advance payment;

- Quality Warranty: One year (excluding wearable parts).

- The shipment packing: 5 X HQ40.

- Installation:

① Engineers will be appointed to guide installation and debugging and train operators;

② Installation salary: USD$80/person/day;

③ Round trip air tickets, food & accommodation: At the cost of buyer;

Total cost for normal is around $3500-4000 (including the air tickets)

- Price validity: 30 days.

- Drawing: please refer to the attachment.