CHD5021TSL Street sweeper

CHD5021TSL Sweeper adopts single engine and driving by complete hydraulic, it is manufactured with advanced technology from famous company. The running of vehicle is flexible with the articulated turning. The standard 240L garbage bin is used to collect garbage and it is equipped with 150L clean water tank. The product fills black of the domestic small sweeper market. It is the minimal dry-wet sweeper, suitable for environmental protection, parking lot, footway and other street.

Performance

1、Complete hydraulic power transmission, all of action can be operated in the cab.

2、The cab is mainly made of glass, the field of vision is open, has air conditioning, roomy and comfortable.

3、The frame is consists of two parts, which is connected by hinge, the design is suitable and the turning of whole vehicle is very flexible.

4、Complete hydraulic turning mechanism, stepless speed change.

5、Sweeping manner: the two brushes are in the front of vehicle, the suction port is in the middle, so that the brushes can sweep garbage to suction port successfully.

6、Suction manner: it adopts filtrating of circular exhausting air, when the air from blower is filtrated by dry filter system, then it will return to suction port for reverse blowing usage, high efficiency, environmental protection and low re-pollution.

7、The sweeper is equipped with 150L clean water tank, turn on the nozzle, which is on the brush bracket, to reduce dust with watering.  is opened to reduce dust when sweeping in the special working area and sweeping dust..

8、The collected garbage is transported into 240L garbage bin. The lifting shelf, controlled by hydraulic, can drop the garbage bin to ground simply and placidly. The operation is convenient.

| Dimension（L*W*H）mm | 3250X1130X2130 |
| --- | --- |
| Total mass（kg） | 1250 |
| Max total mass（Kg） | 1750 |
| Rated engine power（Kw/r/min） | 18/2800 |
| Rated speed（km/h） | 16 |
| Sweeping speed（km/h） | 0～16 |
| Max sweep width（m） | 1.8 |
| Garbage bin volume（L） | 240 |
| Engine model | KUBOTA D1150 Diesel engine |