Inquiry No.: KLE141020DK1A

Date:	2014-10-20

Contact:    Alison Lee

Tel.:        0086-13570460814

Fax:        0086-20-28663078

E-Mail:     crystalivy@gzkoller.com

Quotation

To:

Att.: Cong Trieu Hoang

Country: Vietnam

Tel.:

Fax:

E-mail: trieuhoanglong2013@gmail.com

Price of 1ton Aluminum directly evaporated Ice Block Machines DK10

| Manufacturer | KOLLER | Inquiry No. | KLE141020DK1A |
| --- | --- | --- | --- |
| Payment Terms | T/T | Validity of price | 30 DAYS |
| Item | Product Name | Quantity (SET) | Unit Price (USD) | Delivery time (days) | Amount （USD） |
| 1 | 1tons Aluminum Directly Evaporated Ice Block Machine DK10 | 1 | $8,600 | 30 | $8,600 |
| FOB Guangzhou Port :$ 8,600 USD |

Specification

| SI No. | Description | Details |
| --- | --- | --- |
| 1 | Freezing Time for one ice block | 2 Hours (Approx) |
| 2 | Weight of each Ice Block | 4.5kg |
| 3 | Ice making Capacity | 1,000Kg/Day |
| 4 | Evaporator for ice tank | Freezing Aluminum plate |
| 5 | Insulation tank | Covered with stainless steel sheet |
| 6 | Compressor for Block Ice plant: Make | Copeland |
| 7 | Refrigerant | R 22 ( Freon Based ) |
| 8 | Condenser | Air Cooling condenser |
| 9 | Control and Safety devices | Automatic electric control panel box HP/LP switches with automatic reset, manual reset for oil switch pressure control |
| 10 | Install power | 380V / 3P / 50 Hz |
| 11 | Outside dimensions | 1900mm*1130mm*1100mm |
| 12 | Country of origin | China |

Main parts for our machine are as follows;

- Main refrigeration circuit is made in stainless steel tube, other tube will be copper material but will be painted.

- Stainless steel vibration absorbers on compressors supply and suction line.

- Danfoss expansion valves.

- Liquid receiver with safety valve.

- SPORLAN high efficiency freon filter.

- DANFOSS sight glass with humidity indicator.

- DANFOSS solenoid valve

- ALCO oil seperator

- SPORLAN filter on suction line

Pictures of DK10 1000kg per day

Electrical control box                Aluminum plate ice mould

Company