# DS56-III Corn Flakes Breakfast Cereals Processing Line(120-150kg/h)

Part I/  Machine List:

| Item No. | Descriptions | Quantity(unit) | Technical parameters | Photo |
| --- | --- | --- | --- | --- |
| 1 | Raw material mixer | 1 | output:25kg/once（300kg/h） power:3kw speed of motor:385RPM weight:200kg dimension:1000×500×800mm |  |
| 2 | Screw elevator | 1 | Max.capacity:300-400kg/h power:0.75kw weight:100kg dimension:1600×300×2300mm |  |
| 3 | DS56-III twin screw extruder | 1 | Output:120-150kg/h power: 35kw mode of speed regulation:frequency changer dimension:2500x800x 1800mm |  |
| 4 | Air conveyor | 1 | power:0.55kw weight:3kg speed of motor:2850 rpm max. capacity:450kg/h |  |
| 5 | Hot air roller dryer | 1 | output:300-500kg/h power: 0.55kw weight:100kg dimension:2500x1500x1600mm |  |
| 6 | Air conveyor | 1 | power:0.55kw weight:3kg speed of motor:2850 rpm max. capacity:450kg/h |  |
| 7 | Presser machine | 1 | power:15kw output: 200kg/h weight: 3500kg dimension:1200×1200×3000mm |  |
| 8 | Air conveyor | 1 | power:0.55kw weight:3kg speed of motor:2850 rpm max. capacity:450kg/h |  |
| 9 | SXD three-layer electric dryer | 1 | Transmission motor power:0.55kw Power: 27.5kw capacity:300kg/h weight: 2000kg dimension:4500×1000×700 mm |  |
| 10 | Hoister | 1 | output:300kg/h power:0.37kw weight: 5kg dimension:1500×400×1500mm |  |
| 11 | Material distributor | 1 | output:300kg/h power: 0.4kw weight: 100kg dimension: 1200×500×1000mm |  |
| 12 | Hot air inflating machine | 1 | output: 150kg/h total power: 50kw motor power: 0.75kw weight: 2000kg dimension: 4000×600×2500mm |  |
| 13 | Jacketed pan | 1 | Volume: 100L Power:12 kw Dimension: 1200x800x1400mm |  |
| 14 | Sugar melting machine | 1 | output:600kg/h total power:6kw weight: 500kg dimension:1200×800×1500 mm |  |
| 15 | Sugar sprayer | 1 | power:0.55kw capacity:150kg/h weight: 300kg speed of roller:20RPM dimension:2300×500×1500mm |  |
| 16 | Five-layer dryer(electric) with cooler included | 1 | heating power:40kw capacity:600kg/h weight: 2200kg dimension:18000×800×1800mm |  |

Part II/  Quotations and parameters for full line:

Price of above DS56-III Corn Flakes Processing Line(120-150kg/h) is FOB Qingdao USD98,000/set.

PS: We can also supply natural gas/fuel type dryers for No. 9 & No.16 if you need and price will be usd 6000 higher.

- output: 120-150kg/h.

- installed capacity:118 kw.

- power consumption:88kw.

- length:48m.

- voltage/frequency(3 phases): 380V,50Hz(we can change the voltage if buyer specially request it).

- workers required: 2-4 persons.

- warranty: 1 year from the date of completion of the commissioning.

8.  maintenance manual:provided in English.

Part III/  Remarks :

1. Delivery Term: FOB Qingdao, China.

2. Delivery time:70 days after advance payment is received.

3. Payment Terms: 30% T/T down payment, 70% by T/T before delivery.

4. Common technology and knowledge help including recipes is free of charge with this line from us.

5. Materials of the surfaces for the full line and all the parts that contact food is made of stainless steel at food grade.

6. Installation/testing/operation after-service will be supplied. We will send 2 experienced technicians for installation, trial run and training your workers for about 10-20 days. The fees of roundtrip air tickets, food and accommodations in buyer’s site and allowances of usd 60/day/person will be covered by the buyer.