Price list of complete set equipment for A pp

Woven bag making plant with bag output 15 million/year

Description              type        unit price    Qty.   amount

- Flat Yarn Extruder     YF-SPL -110/30/1200    ￥778800   1       ￥778800

H.S code:8444009000

- Single-spindle winding machine  S-SDC-208A ￥299520    1      ￥299520

H.S code:84454090

- Four shuttle Circular loom  YF-BT/BC-750/6  ￥31200    24      ￥748800

H.S code:84462190

- Drying mix machine       YFJ-50          ￥6000       1    ￥6000

H.S code:8419399090

- Recycle Granulator       SJ-FL150-II       ￥46800      1    ￥46800

H.S code:84772010

- Lamination Machine       SJ-FMF90/1000     ￥172800     1    ￥172800

H.S code:84778000

- Gravure Printing Machine        YF-AY6800        ￥142800    1     ￥142800

H.S code:84425000

- Manual Bag Cutting             CD-II            ￥3180          3      ￥9540

H.S code:84778000

- Sewing Machine                GB8-2          ￥2100           8      ￥16800

H.S code:84522900

- Hydraulic Baling Press           KS-850          ￥15780        1      ￥15780

H.S code:8422400

- Industrial Water Chiller       SFL-05S       ￥10800       1     ￥10800

H.S code:8418699090

- Cooling Tower                  SF-50T       ￥16500      1      ￥16500

H.S code:8418699090

12. 6 Colour Printing Machine      YF-RY6800    ￥130800      1    ￥130800

H.S code:84431500

13.Auto-Cutting & Sewing Machine  YF-SCD-1200*800       1      ￥154800

H.S code:84778000

- Spare parts                              ￥240000           ￥240000

15.Steel Bobbin                                   ￥2.1       50000     ￥105000

Total                                                       ￥2895540

The above price is based on FOB wenzhou factory china excluding installation charge

Country of Supply/Origin: China

Type of Packing: Packed in nude

Warranty Period: One year except quick-wear parts.

Term of Payment: 30%T/T as the advance, 70%T/T before the delivery.

Delivery Period: Within 30~40 days after we receive the advance payment or L/C

Installation: The buyer provide each technician the accommodation, the round-trip ticket, visa and salary $65/person/day.

Flat Yarn Extruder and Single Spindle Winder

YF-SPL series flat yarn extrusion line is designed and developed on the base of introducing and assimilating the up-to-date technologies at home and abroad.

It adopts the international electric digital-simulation control technology such as computer-controlled frequency conversion speed regulation so as to make the main target reach the international advanced level.

Meanwhile, with high production efficiency and high quality of tape tube forming, as required, this assembly can also be equipped with advanced filter change structure as well as fibrosis structure that is used for producing flexible packaging bags or fibrosis sewing thread.

This line has two kinds of stock thread heating structures, i.e. hot-blast stretching oven and electric baking board for customers’ alternatives. Applied to a wide range, it can be used for the forming of PP, HDPE and LLDPE flat yarn.

Main Technical Parameters

| Model No. | YF-SPL-110/30/1200 |
| --- | --- |
| Max. Extrusion Output (kg/h) | 380 |
| Screw Diameter (mm) | 110 |
| Ratio of L/D | 30:1 |
| Rotational Speed of Screw (r/min) | 20-120 |
| Width of Die Lip (mm) | 1200 |
| Max. Linear Speed (m/min) | 280 |
| Flat Yarn Denier Scope (tex) | 60-200 |
| Drawing Ratio | 4-10 |
| No. of Winder (Spindles) | 208 |
| Dimension of Bobbin (D×L) (mm) | 38×230 |
| System Installed Power (kw) | 320 |
| Normal Consumption Power (kw) | 170 |
| Installing Dimensions (L×W×H) (mm) | 34000×3800×3200 |
| Approx. Weight (kg) | 30000 |

Oil-free Little Cam Four-shuttle Circular Loom

1. Small cam type and convex table as well as swing-beam rolling wheel transmission is adopted, making it easy and stable to run.
2. Slide block and rod are eliminated while the wearing parts are decreased. Rolling transmission is adopted in entire structure, which doesn't need lubricant.
3. Frequency speed regulation which is convenient and stable is adopted.
4. It is configured with automatically stop detecting unit when meeting the situation of warp/weft breaking, weft ending. The stoppage unit is sensitive and reliable.
5. It's an environmental product whose noise is not more than 80dB(A).
6. Low strength plastic yarn which is made from 100% regenerated plastic can be adopted to weave.
7. It is high-efficient and energy-efficient. The highest rotation speed of the main motor can reach 180r/min and the power is 1.5/2.2kw, which can save 10 thousand degree electricity compared with the traditional four shuttle circular loom whose power is 4kw.
8. It is a patent device. (Patent No.: ZL 200820166333.1)

Main Technical Parameters:

| Model No. | YF-BT/BC-750/4 |
| --- | --- |
| Number of Shuttle | 4 |
| Folding Width of Weaving (mm) | 350-750 |
| Max. Number of Warp | 640/768 |
| Rotational Speed of Main Body (r/min) | 140-180 |
| Production Capability (m/min) (40 warps /100mm)) | 1.4-1.8 |
| Power of Main Motor (kw) | 1.5-2.2 |
| Gross Power of Motor (kw) | 2/2.7 |
| Approx. Weight (kg) | 1800 |
| Installing Dimensions (L×W×H) (mm) | 8300×2200×2730 |

Laminating Machine

- Making use of the good adhesive property of polypropylene & polyethylene at melting status, the machine adheres and laminates paper or color-printed OPP & CPP film to woven bag under pressure, and through cutting-off and sewing to make paper & plastic laminated or color-printed packaging woven bags.

- The extruder, with helical gear reducer of 20CrMnTi alloy steel and the screw &cylinder made of nitrided 38CrMoA1A alloy steel adopts automatic temperature control system to adjust melting temperature. Width of coating & laminating can be regulated, and stepless speed regulation is to control coating thickness and laminating speed, 6 stations for material feeding. The pneumatic-hydraulic edge correction for rewinder assures the accuracy of coating.
Pneumatic roller can assure even pressure. Frictional winding device is equipped.

Main Technical Parameters:

| Model No. | SJ-FMF120/1500 |
| --- | --- |
| Diameter of Screw (mm) | 120 |
| L/D Ratio of Screw | 28:1 |
| Number of Die | 1 |
| Width of Die (mm) | 1500 |
| Gross Power (kw) | 96 |
| Motor Power of Extruder (kw) | 37 |
| Heating Power of Extruder (kw) | 42 |
| Power of Driving Motor (kw) | 11 |
| Max. Coating Width (mm) | 1200 |
| Coating Speed (m/min) | 30-100 |
| Installing Dimensions (L×W×H) (mm) | 15500×8000×2500 |
| Approx. Weight (kg) | 10000 |

Note:

1. Part 3 stops production, the lamination machine only include part 1 and part 2.

2. Kraft or Bopp film can be laminated with PP fabric.

Gravure Printing Machine

The machine is suitable for printing BOPP, PET, PVC, LDPE, HDPE films, Al foil and web rolls with good printing performance.

It can complete multi-color printing by one step, through color register, color printing and winding at continuous speed regulation. The tension regulation of winding and let-off adopts automatic control.

It adopts double drying ovens with far-infrared drying, which makes the drying fast, and has got the advantages of quick printing and accurate color register and vivid picture.

The finished product can be used for plastic packaging bag directly, or laminated with another materials to make color printed woven bag and cartons etc.

Main Technical Parameters:

| Model No. | YF-AY6800 |
| --- | --- |
| Printing Width (mm) | ≤800 |
| Printing Length (mm) | ≤1200 |
| Printing Speed (m/min) | 5-100 |
| Register Tolerance (mm) | ≤0.15 |
| Printing Color | 1-6 |
| Gross Motor (kw) | 80 |
| Installing Dimensions (L×W×H) (mm) | 9500×2200×2500 |
| Approx. Weight (kg) | 9000 |

Flexographic Printing Machine

Adopting soft sensitive resin as its printing plate, this kind of aniline printing machine can be used to print PP/PE woven cloth tube, PP/PE film tube, cellophane and web, which is an ideal equipment for printing PP/PE woven cloth, non-woven cloth, shopping bags, vest bags as well as garment bags.

1. Easy operation, flexible start, accurate register.

2. The meter-counter can preset printing quantity so that the machine stops automatically when the preset number is reached or the material is run out.

3. Lift and lower the printing rollers manually or automatically and the printing ink can automatically stir after being lifted so as to avoid being dried and frozen.

4. The printing ink is transmitted by cobweb cylinder, which assures even ink color.

5. Its reliable drying system working in harmony with high-speed running can automatically turn off once the machine stops.

6. 360℃ continuous and adjustable longitudinal register plate.

7. Inverter motor for speed regulation adapts to different printing speed.

8. Buttons for “JOG” and “STOP” on roller base and rewinding stand are convenient to operate the machine while installing the plates.

Main Technical Parameters:

| Model No. | YF-RY6800 |
| --- | --- |
| Max. Diameter of Unwinding Roll (mm) | 1200 |
| Max. Width of Unwinding Roll (mm) | 800 |
| Max. Printing Width (mm) | 700 |
| Printing Length (mm) | 230-1200 |
| Max. Printing Colors | 6 |
| Printing Speed (m/min) | 5-50 |
| Gross Power (kw) | 15 |
| Approx. Weight (kg) | 4500 |
| Installing Dimensions (L×W×H) (mm) | 6000×1800×2400 |

Automatic Cutting and Sewing Machine

1. It automatically accomplishes the heat cutting and bottom hemming at fixed length for color-printed or plain woven cloth roll, which saves much labor forces.

2. It adopts touch screen for presetting, PLC for controlling and servo motor for driving in order to control the length of sack precisely.

3. The mouth of bag is easy to open and won’t be conglutinated after heat cutting.

4. With automatic counting, the finished sacks can be delivered in batches.

5. With pneumatic roll-installing, it’s so convenient to operate.

| Model No. | YF-SCD-1200×800 |
| --- | --- |
| Max. Diameter of Cloth Roller (mm) | 1200 |
| Cutting Length (mm) | 600-1200 |
| Folding Width (mm) | 20-30 |
| Gross Power (kw) | 6 |
| Max. Cutting Width (mm) | 800 |
| Cutting Precision (mm) | ±4 |
| Production Capacity (pcs/min) | 20-40 |
| Approx. Weight (kg) | 2200 |
| Outline Size (L×W×H)(mm) | 5100×4500×1200 |

Manual Bag-cutting Machine

This machine can cut the woven cloth in rolls into sheet as required.

| Model No. | CD-III |
| --- | --- |
| Max. Width of Cloth Roller(mm) | 2100 |
| Weight of Cloth Roller(kg) | ≤1000 |
| Power of Thermal Cutting (kw) | 15 |
| Power of Motor(kw) | 1.5 |
| Installing Dimensions(L×W×H) (mm) | 7000×2500×1500 |
| Approx. Weight (kg) | 600 |

Sewing Machine

This machine can hem the bottom and top of the bag.

| Model No. | GK4-1 |
| --- | --- |
| Max. Sewing Speed(r/min) | 1400 |
| Stitch Type | Double Lock Stitch |
| Length of Thread (mm) | 9-14 |
| Max. Sewing Thickness(mm) | 14 |
| Power of Motor (kw) | 0.55 |
| Applied Range | Container Bag |

RECYCLING GRANULATOR SJ-FL120-II

MAIN TECHNICAL SPECIFICATIONS:

Model:                             SJ-FL120-II

Diameter of screw:                    120MM

L/D ratio of main screw:                 10:1

L/D ratio of sub-screw:                  6:1

Power of main motor:                  18.5KW

Power of sub-motor:                   7.5KW

Rotational speed of screw:             50-80R.P.M

Gross heating power:                  12KW

Production capacity:                  40-80KG/H

Power of cutting:                     1.1KW

Heating power:                       12KW

Installing dimensions (L×W×H):   4500×2000×1100MM

Weight:                             1200KG

HYDRAULIC BALING PRESS KS-850

Main parameter:

Model:                       KS-850 (HYDRAULIC)

Working pressure:                 6-8MPA

Power of motor:                    2.2KW

Height of bag overlapping:           900MM

Install dimensions (L×W×H):  2000×930×2600MM

Weight:                          1000KG

| Production Capacity (pcs/min) | 20-40 |
| --- | --- |
| Approx. Weight (kg) | 2200 |
| Outline Size (L×W×H)(mm) | 5100×4500×1200 |

Drying Mixer

This machine can dry and mix materials of polypropylene& polyethylene for machines of tape drawing, film extruding and plastic laminating.

| Model No. | yfj-50 |
| --- | --- |
| Size of Hopper (D×H) (mm) | 600×600 |
| Production Capacity (kg/h) | 200 |
| Power of Motor (kw) | 15-18.5 |
| Installing Dimensions (L×W×H) (mm) | 1250×700×1100 |
| Approx. Weight (kg) | 300 |

Industrial Water Chiller

Industrial water chillers are designed in case type, which has totally-enclosed case shell. It can be placed directly on the working site, keep constant and smooth running under changeable temperature outdoors and prevent dust from influencing heat elimination.It adopts shell and tube style, manufactured by latest CAD/CAM design and CNC processing center.

It adopts the most advanced European original screw compressor and high-efficiency heat exchanger in the world. It is widely used in the field of plastic industry, electroplating industry, printing industry, etc.

Different models can be designed according to customers’ requirements.

| Model | SFL-05S |
| --- | --- |
| Cooling Capacity | 14285W 12300Kcal/h 48806.4Btu/h |
| Input Power (kw) | 4.3 |
| Refrigerant | R22(404A) |
| Cooling Water Flow(m3/h) | 67 |
| Cooling Water Outlet & Inlet(in) | 11/2” |
| Cooling Water Temperature | ≤40℃ |
| Chilled Water Flow(L/min) | 60 |
| Chilled Water Outlet & Inlet(in) | 1” |
| Water Tank Storage(L) | 130 |
| Installing Dimensions (L×W×H) (mm) | 1280*680*1300 |
| Approx. Weight(kg) | 145 |

Cooling Tower

| Model No. | SF-50T |
| --- | --- |
| Flow (m3/h) | 50 |
| Fan Diameter (mm) | 1190 |
| Theoretical Air Quantity(m3/h) | 18000 |
| Motor Power (kw) | 1.5 |
| Motor Ranting Current (A) | 4.4 |
| Tower Height (mm) | 2400 |
| Max. External Diameter (mm) | 2200 |
| Net Weight (kg) | 368 |
| Running Weight (kg) | 730 |