| To: |  |
| --- | --- |
| Attn.: | Mr.Witoso Tansari |
| Address: | Indonesia |
| Tel.: | 62-216254218,62-216256767 |
| Fax.: |  |
| E-Mail: | witoso_tansari@yahoo.com |

Inquiry No.:KLE141110CV5A

Date	2014-11-10

Contact:	Anna

Tel.:       86-18126832529

Fax:       86-20-34922345

E-Mail:   rkollerice07@gzkoller.com

QUOTATION

Dear Mr.Witoso Tansari,

In compliance with your request，we offer the price and detailed information for 5tons capacity cube ice machine (CV5000) for your reference as follows.

1. Quotation for Cube Ice Machine CV5000:

| Manufacturer | KOLLER | Inquiry No. | KLE141110CV5A |
| --- | --- | --- | --- |
| Terms of Payment | T/T | Validity of price | 30 DAYS |
| Item | Products’ Name | Quantity (SET) | Unit Price (USD) | Weight (kg/unit) | Delivey Time (Days) | Amount（USD） |
| 1 | 5 tons/day Cube Ice Machine CV5000 | 1 | $27,000 | 1,780 | 30 | $27,000 |

Note:

1. The above-mentioned price is FOB Guangzhou port price.

2. Terms of payment: T/T, 50% of total value is in advance by T/T; 50% will be paid before shipment.

3. Packing: in standard plywood case for CV5000 ice cube maker, cooling tower will be shipped by completely knocked down.

4. Installation: We will install and test the machine before shipping, you just need to install cooling tower, connect water pipes and power to start production. CD and operation manual will be provided to guide the installation. If requested, we can send one engineer to guide the installation and train your staff how to operate. It is free of charge within 5 days. Beyond 5 days, we will charge $100 USD per day for one person as service fee. The buyer needs to afford the round-trip tickets and visa fee for our engineer.

Meanwhile, the accommodation and food at the installation space should be provided by the buyer.

5. Warranty: We provide 12 months warranty for our machine. For after sales service, once the machine is out of work, you can send us pictures or video about the fault, we will mail you the solution to solve problems to save time. Or we also can send one engineer to your place for door to door-to –door service. If the parts is broken and proved by our engineer for non-personal reason, we will offer free parts to replace within guarantee period; if it is beyond guarantee period, we will charge market price for the new parts.

6. Delivery time: within 30 working days after receiving the deposit.

7. The above price has included the cooling tower, water pipes, water pumps and accessories.

8. Operational manual and CD will be offered to guide the installation by English and Chinese and Arabia.

2. Working Conditions for Cube Ice Machine CV5000:

| 1. Max. Ambient temp. | +400C |
| --- | --- |
| 2.Relative humidity | 85% |
| 3.Supply water temp | 210C |
| 4.Power supply | 380V/3Phase/50Hz |
| 5.Refrigerant | R22 |
| 6.Compressor type | Semi-hermetic piston compressor |
| 7.Cooling system | Water cooling condenser |

3. Performance Parameters for Cube Ice Machine CV5000:

| NO. | Parameters | Technical data |
| --- | --- | --- |
| 1 | Name | Cube Ice Machine |
| 2 | Model | CV5000 |
| 3 | Quantity | 1Units |
| 4 | Daily output | 5tons/day |
| 5 | Weight | 1780kg |
| 6 | Measurement | Cube ice machine | 3110mm*1940mm*2040mm |
|  |  | Cooling tower | 1775mm*1775mm*1800mm |
|  |  | Cube ice | 22mm*22mm*22mm/29mm*29mm*22mm |
| 7 | Noise | 55dB |
| 8 | Refrigerant | R22 |
| 9 | Evaporating temp. | -10℃ |
| 10 | Condenser temp | +40℃ |
| 11 | Input water temp. | 21℃ |
| 12 | Ambient temp. | 40℃ |
| 13 | Compressor | Model | Semi-hermetic piston compressor |
|  |  | Brand name | Bock(Germany) |
|  |  | Amount | 1 |
|  |  | Type | HG6/1240-4 |
|  |  | Capacity | 25HP |
| 14 | Cooling tower | Water flow | 31.2m3/h |
|  |  | Air flow | 280CMM |
|  |  | Headloss | 16 Kpa |
|  |  | Motor power | 1.5KW |
| 15 | Power of ice conveyor motor | 0.75KW |
|  | Power of cooled water pump | 4KW |
|  | Power of circulating water pump | 1.5KW |
| 16 | Evaporator | Type | Cube type |
|  |  | Quantity | 18 pieces |
| 17 | Control system | PLC micro-computer control |
| 18 | Material for mainframe | Stainless steel 304 |

Note: the CV5000 ice cube machine will have 100% capacity under input water temperature 210C, ambient temperature 250C.

4. Components List of Cube Ice Machine CV5000:

| Item | Name of Components | Type | Quantity | Brand Name | Original Country |
| --- | --- | --- | --- | --- | --- |
| 1 | Compressor | HG6/1240-4 | 1 | Bock | Germany |
| 2 | Evaporator | VEP-CV-50 | 18 | Koller | China |
| 3 | Water cooled condenser | XMR-WN-40 | 1 | XUEMEI |  |
| 4 | Refrigeration components |  | 1 butch | DANFOSS/CASTAL | Demark/Italy |
| 5 | PLC Program control | TD400C | 1 | SIMENS | Germany |
| 6 | Electrical components |  | 1 butch | LG (LS) | South Korea |
| 7 | Phase Protector |  | 1 | Standard | China |
| 8 | Expansion Valve |  | 1 | Danfoss | Denmark |

5. layout of ice cube machine project:

Layout of ice cube machine installation

6. Components list for Ice Cube Machine:

| Item | Name of Components | Brand Name/ Original country | Picture |
| --- | --- | --- | --- |
| 1 | Compressor 压缩机 | Bock/Germany 比泽尔/德国 |  |
| 2 | Electrical components 电器配件 | LG (LS)/ South Korea LG/LS / 南韩 |  |
| 3 | Expansion valve 膨胀阀 | DANFOSS/ Denmark 丹佛斯 / 丹麦 |  |
| 4 | Solenoid Valve 电磁阀 | CASTEL/Italy 卡士妥 / 意大利 |  |
| 5 | High/Low Pressure Gauge 高低压力表 | DANFOSS/Denmark 丹佛斯 / 丹麦 |  |
| 6 | Water pump 水泵 | YL/China 中国 |  |
| 7 | PLC program controller PLC 程序 | Siemens/Germany 西门子 / 德国 |  |
| 8 | Ice maker grids 制冰器 | Koller/China 中国 |  |

7. Pictures:

5 tons/day cube ice machine CV5000

PLC control system                        Ice making grids

Cooling tower                                        Cube ice

Screw conveyor                               Ice storage bin

Digital Scale                          Sealing machine

Packed cube ice                      Cube ice stored in cold room

Ice making process

Ice cube machine installation drawing

Layout of CV5000 cube ice machine

8. Cube Ice Machine Projects:

5 tons / 10 tons cube ice machine in South Africa & 3 tons cube ice machine in Saudi Arabia

3 tons/ 5 tons cube ice machine in Angola   Testing of 20 tons cube ice machine in our factory

9. Koller Company:

Factory                                 Workshop

Office building                                 Sales team

CE Certificate                                 ISO9001 Certificate

Excellent Brand of China Ice Machine Industry

The Drafting Committee of National Ice Machine Industrial Standard

Produce & Academic Research Strategy Cooperation Partner with Tsing Hua University.