济南赛信机械有限公司

JINAN SAIXIN MACHINERY CO.,LTD.

Email: jnsaixin@hotmail.com

济南市高新开发区环保科技园正丰大厦

Zhengfeng Building,Jinan High-tech Industrial Development Zone,Jinan,Shandong,China

Tel:0086-531-88269073/15853107621                     Fax:0086-531-88970662

XBF-III AUTOMATIC INSTANT NOODLES PROCESSING LINE

I.  The total length of the line is about 23 meters and this line can be installed turning right-angle. The line consists of dough maker/host machine/boiling machine/ automatic electric fryer and cooler.

II.  TECHNICAL PARAMETERS:

1/  dough maker

rotating paddle diameter：￠490mm

rotating paddle speed：140r.p.m

power：3Kw

maximum capacity：25kg/one time

2/  host machine/compound shaper

  - rolling and pressing machine

width：210mm

capacity：150kg/h

power：2.2kw

dimension（L×W×H）:1400×600×1250mm

  - automatic cutting and shaping machine

technical parameters：

cutting knife diameter：￠37.5mm

speed：101r/min

3/ boiling machine

- boiling part

effective convey length：5m

convey speed：infinite variable speed

boiling time：70～90 seconds

boiling temperature：96～98℃

capacity：180kg/h

power：45Kw

dimension（L×W×H）:8000×440×1250mm

4/ cutting machined

cutting knife diameter：￠80mm

speed：28 round/minute

5/ automatic electric fryer

speed：adjustable

temperature：150℃

frying time：60～90 seconds

power：36Kw

oil consumption ratio：20～22%

dimension（L×W×H）:3300×600×1300mm

6/ cooler

effective length：3m

convey speed：adjustable

power：supplied by fryer

cooling power：3×30W

gas release quantity：3×28m3/min

dimension(L×W×H):3080×500×1100mm

III . Manufacturing process chart

Material mixing

↓

Flour,salt,water etc.→mixing→laid about 20 minutes→pressing and shaping →boiling	→cutting and folding →	frying→	cooling→ finished products

IV. Quotation:

The price of the XBF-III instant noodles processing line(35000pcs/24h) is FOB Qingdao USD26,800/set(electric type) and USD28,800/set(steam type) . Materials of the surfaces for the full line and all the parts that contact food is made of stainless steel at food grade.

V. Remarks :

1. Delivery Term: FOB Qingdao, China.

2. Delivery time: 30 days.

3. Payment Terms: 30% T/T down payment, 70% by T/T before delivery.

4. All technology and knowledge help including recipes is free of charge with this

line from us.

5. Installation/testing/operation after-service will be supplied. We will send 1

experienced technicians for installation, trial run and training your workers for about

7-10 days. The fees of visa,roundtrip air tickets, food and accommodations in

customer’s site with allowance of 60USD/day/engineer shall be covered by buyer.