MACHINE PICTURES

DCJ-240 machine, 4-side sealing with heating hopper to keep honey temperature

Technical Specification (FCA Port Shanghai price in US$)

| Item | Description of Item | Unit Price | Qty. | Total Price |
| --- | --- | --- | --- | --- |
|  |  | in USD |  | in USD |
| 1 | Machine | Automatic Paste Packing Machine | 5500 | 1 | 5500 |
|  | Model | DCJ-240 |  |  |  |
|  | Sealing type | 4-side sealing |  |  |  |
|  | Measurement | Mechnical piston pump type (0-20ml, 10-30ml, 30-100ml depend on requested) |  |  |  |
|  | Cutting type | Zigzag cutter with tear notch |  |  |  |
|  | Product | Honey need heating jacketed hopper |  |  |  |
|  | Hopper and volume | Heating jacketed hopper with separate temperature controller, 20L |  |  |  |
|  | Sealer | Horizontal sealer: line Vertical sealer: diamond |  |  |  |
|  | Packing speed | 40 - 60bag/min （Depend on Products） |  |  |  |
|  | Bag size | W:30-110mm(through change bag former) L:30-170mm(adjustable through panel) |  |  |  |
|  | Total power | 2050W |  |  |  |
|  | Voltage | 220V or 380V |  |  |  |
|  | Machine Net Weight | 200Kg |  |  |  |
|  | Machine size | L×W×H： (625x751x1558)mm |  |  |  |
|  | Material | Stainless steel 304 |  |  |  |
|  | Includes | Inverter, photo sensor, short output belt conveyor, a bag former |  |  |  |
|  | Optional | Ribbon printer, | 250 | 1 | 250 |
| Features Bag-making, measuring, filling, sealing, cutting and counting are all finished automatically. 2. Either under set length control or photo-electronic color tracing, we set bag length and cut in one step. Time and film saving. 3. The temperature is under independent PID control, more suitable for different packing materials. 4. The driving system is simple and reliable, and maintenance is easy. 5. Applicable material should be composite films like: PET/PE, Paper/PE, PET/AL/PE, OPP/PE. |

Guarantee: One year from the date of shipment against any manufacturing defects

Shipment: Within 10 working days from receiving 30% deposit

Payment:T/T, 30% deposit in advance and full payment before delivery

DETAILS PICTURES

- Sealing and cutting part with tear notch

2. Paste dosing system – plunger pump kind

It is volume way not weigh. You can get different volume (ml) after pump adjusted.

3.Date coding ribbon printer

4. sample bag

5.heating jacketed hopper

Electrical Element List

| Name of Equipment | Factory Brand | Picture | Quantity |
| --- | --- | --- | --- |
| Inverter | China ENC |  | 1 set |
| Decelerates motor | China Taiwan Gongji |  | 1 set |
| Step motor | China Jintan Sihai |  | 1 piece |
| Step motor driver | China Jintan Sihai |  | 1 piece |
| Temperature controller | China Shanghai Yatai |  | 2 pieces |
| Pulling film motor | China Linix |  | 1 piece |
| Photo sensor | China Longyi |  | 1set |
| Induces switch | Taiwan Roko |  | 4 pieces |
| Solid state relay | France Schneider |  | 19 pieces |
| Thermocouple | China ordered |  | 2 pieces |
| Pneumatic element | China Taiwan AirTAc |  | 1set |
| Bearings | Main from German and Japan |  |  |

Tool box (includes free part, free tools and doc)

- Free part with Machine

| Item | Description of Item | Qty. |
| --- | --- | --- |
| 01 | Gum over (fix the film etc) | 02 |
| 02 | Solid relay | 01 |
| 03 | Heat pipe | 04 |
| 04 | Thermocouple | 02 |
| 05 | Proximity switch | 01 |
| 06 | Zigzag jaw | 01 |
| 07 | Fuse(set) | 01 |

- Free tooling with Machine

| Name | Spec | QTY |
| --- | --- | --- |
| socket head wrench | STD | 1set |
| cross screwdriver |  | 1Pc |
| straight screwdriver |  | 1Pc |
| screwdriver |  | 1Pc |
| scissors |  | 1Pc |
| copper brush |  | 1Pc |
| hairbrush |  | 1Pc |
| Toolbox |  | 1Pc |

- Doc with Machine

| Name | Spec | QTY |
| --- | --- | --- |
| Manual | According to ordered machine | 1 |
| Certificate of Quality |  | 1 |
| Frequency conversion manual |  | 1 |
| Temperature controller Manual |  | 1 |
| Proxmity switch Manual |  | 1 |

# Text boxes

Features

1. heating code printer

2. three lanes

3. each lane can put 13 codes (each code W2mm H3mm)

4. easy to change codes (0-9, A-Z)

5. Use ribbon, each roll 100m

6.There is alarm of ribbon lack

separate temperature controller for heating jacketed hopper, which one you can set temperature depend on material

Honey sample pouch

(3-side sealing)