PP Woven Bag Production Line (5 Millions Per Year)

| Description | Model No. | Unit Price | Qty. | Amount |
| --- | --- | --- | --- | --- |
| 1.Plastic Tape Drawing Machine | SJ-FS110/800B | $24800 | 1SET | $24800.00 |
| 2.Cam type winding machine | S-STL-II/150 | $9750 | 1SET | $9750.00 |
| 3.Four Shuttle Circular Loom | YF-XT-750/4 | $5200 | 10SETS | $52000.00 |
| 4.Drying Mixer | YFJ-50 | $1000 | 1SET | $1000.00 |
| 5.Auto feeder | XTL300 | $680 | 1SET | $680.00 |
| Recycling Granulator | YF-FL120-II | $7250 | 1SET | $7250.00 |
| 7.3-color printing | S-YFY-800IIIB | $5580 | 1SET | $5580.00 |
| 8.Hydraulic Baling Press | KS-850 | $2630 | 1SET | $2630.00 |
| 9.Auto Sewing Machine | YF-FM800 | $4050 | 1SET | $4050.00 |
| 10.Auto Bag-cutting Machine | SQJ II-800 | $4050 | 1SET | $4050.00 |
| 11.Tape winding bobbin | 38x230mm | $0.35 | 20000PCS | $7000.00 |
| 12.Spare parts |  | $10000 | A Lot | $10000.00 |
| TOTAL FOB WENZHOU |  |  |  | $128790.00 |

The above machines are aiming to make the ordinary PP woven bag, packing something like rice, wheat, animal feed, etc. The prices are all quoted upon the FOB Wenzhou terms. If you have any other individual requirements, please inform me of it.

Country of Supply/Origin: China

Type of Packing: Packed in nude

Terms of Payment: 30%T/T as the advance, 70%T/T before the delivery or 100% by irrevocable L/C at sight

Delivery Period: Within 50 days after we receive the advance payment or L/C

Installation: The buyer provide each technician the accommodation, the round-trip ticket, visa and salary $65/person/day.

Warranty Period: One year except quick-wear parts.

Raw material: PP(polypropylene), raffia grade ( MFI less than 5.0 grams/10 minutes)

FLOW CHART OF PRODUCTION

- PLASTIC TAPE DRAWING MACHINE

SJ-FS110/800B:diameter of screw(mm):110

L/D ratio of screw:23:1

Rotational speed of screw(r/min):25-75

Widtn of the die(mm):800

Motor power(kw):30

Heating power of extruder:36

Power of driving of extruder:7.5

Heating power of the motor:15

Drawing rate oven(kw):4-8

Thickness of tape(mm):0.025-0.08

Capacity(kg/h):50-100

Linear speed:80-200(r/min)

Installing dimensions(L*W*H):13300*1500*2000

Weight:6500kg

2.Cam tape winding machine

S-STL-II/150:layer no.of spindle :5

No.of spindle:150

Dimension of bobbin(D*L)(mm):38*230

Linear speed of tape winding(m/min):80-150

Power of main motor(kw):2

Power of winding motor(kw):7

Installing dimensions(L*W*H)(mm):5000*1500*1700

Weight:3000kg

3.Swing arm type oil- free little cam six-shuttle circular loom

Characteristic: no slider bar  no sliding block  low energy consumption  low nosiy

- Small cam type and convex table as well as swing-beam rolling wheel transmission is adopted. And less easy broken part.

- slide block and rod are eliminated while the wearing part are decreased

- Rolling transmission is adopted in entire structure, which doesn’t need lubricant.

- the rotational speed of main motor is 180r/m,the power is 1.5/2.2kw which is save 10thousand degree electricity compare with the 4kw motor

- low strength plastic yarn which is made from 100% regenerated plastic can be adopted to weave.

- adopt double-sets aluminum sit, make it easy to change the bear and swing bar

YF-XT-750/4:Number of shuttle: 4

Folding width of weaving(mm): 350-750

Max. Number of warp: 640/768

Rotational speed of main motor(r/min): 140-180

Capacity(meter/min ):1.4-1.8

Power of main motor(kw): 2.2

Total power(kw): 2.7

Weight(kg): 1800

Installing dimension(L*W*H)(mm): 8300*2200*2730

4.Drying Mixer

YFJ-50: Size of hopper (D*H) (mm);500*600

Production capacity (kg/h):200

Power of motor (kw):15-18.5

Installing dimensions(L*W*H)：1250*700*1100

Weight(kg): 300

5.Auto Feeder

The machine can deliver dried material to the hopper of extruder so as to reduce labor intensity and also can feed materials with fixed quantity in fixed time.

XTL300:Material-feeding Manner:Spiral manner

Power (kw):1.1

Installing Dimensions (L×W×H) (mm):2700× 1200× 2000

6.Recycling Granulator

SJ-FL120-II: Diameter of screw (mm):120mm

L/D ratio of screw: main screw10:1

Rotational sped (r/min):50-80

Power of motor (kw):18.5

Power of sub-motor (kw):7.5

Motor power of gain cutting (kw):1.1

Heating power (kw):12

Production capacity (kg/h):40-80

Installing dimensions (L*W*H)(mm):4500*2000*1100

Weight(kg): 1200

7.Relief offset press for pp woven sack

S-YFY-800IIIB：max.input width(mm): 800

Max printing width (mm):660

Max printing length (mm): 1200

Thickness of rubber relief printing plate(mm):4

Diameter of printing roller(mm):480

Printing capacity(pcs/h): 1000-2000

Printing color number: 3color

Power of motor (kw): 2.2

Installing dimensions (L*W*H)(mm):3400*1400*1300

Weight(kg): 2000

8.Hydraulic baling press

KS-850：Working pressure (mpa):6-8

Power of motor (kw):2.2

Height of bag over lapping (mm):900

Installing dimensions (L*W*H)(mm):2000*930*2600

Weight(kg): 1000

9.Sewing Machine

YF-FM800: Max. width of bag (mm):800mm

Max. length of bag (mm):1300mm

Production capacity(pcs/min):20-30

Folding width(mm):16-25

Length of stitch(mm):9-16

Max. Sewing thickness(mm):8

Gross power(Kw):2

Installing dimensions (L*W*H)(mm):4500*2500*1200

Weight(kg): 700

10.Automatic Bag-cutting Machine

This machine can cut the woven cloth in rolls into sheet automatically as required, which is specially used for rice bags, cement bags, fertilizer bags, sugar bags, animal feed bags, etc.

It is simple and easy to operate and maintain. It reduces labor intensity, improves the production efficiency, which is an ideal equipment for bag making factory.

SQJ II-800: Max. Cutting Width (mm):800

Weight of Cloth Roller (kg):≤200

Power of thermal cutting(kw):3

Power of Main Motor (kw):2.2,0.75

Cutting Speed (pcs/min):30-60

Installing dimensions (L*W*H)(mm):6000×2000×1500

Approx. Weight (kg): 600

Remark:Heat-cutting