Quotation

Description                                    type            unit price

Circular Double-sided Printing Bag-making Machine  YF-ZD/A          $29800

Automatic Cutting & Sewing Machine    YF-SCD-1200×800           $25800

The above price is based on FOBwenzhou port china excluding installation charge and commision.

Circular Double-sided Printing Bag-making Machine

This machine, matched with laminating machine or not, is used for making laminated cement bag and various kinds of laminated PP woven bags.

It has the functions of printing, perforating, gusseting, flat-cutting, 7-type cutting, pneumatic-hydraulic auto edge correction for material feeding and has the advantages of high production efficiency, reasonable structure, easy maintenance and perfect printing.

It is the ideal equipment for making laminated bags and cement bags.

| Model No. | YF-ZD/A |
| --- | --- |
| Max. Input Width (mm) | 750 |
| Max. Printing Width (mm) | 600 |
| Bag Making Length (mm) | ≤ 1200 |
| Bag Making Width (after edges folded) (mm) | 300-500(600) |
| Output (pcs/min) | 60-150 |
| Double-side Printing Colors | 1-4(6) |
| Power of Motor (kw) | 4 |
| Drying Power (kw) | 10 |
| Fold Form | displacement or not |
| Error of Edges Folded | ≤ 3mm |
| Installing Dimensions (L×W×H) (mm) | 10300×1600×2200 |
| Approx. Weight (kg) | 5500 |

Automatic Cutting and Sewing Machine

1. It automatically accomplishes the heat cutting and bottom hemming at fixed length for color-printed or plain woven cloth roll, which saves much labor forces.

2. It adopts touch screen for presetting, PLC for controlling and servo motor for driving in order to control the length of sack precisely.

3. The mouth of bag is easy to open and won’t be conglutinated after heat cutting.

4. With automatic counting, the finished sacks can be delivered in batches.

5. With pneumatic roll-installing, it’s so convenient to operate.

| Model No. | YF-SCD-1200×800 |
| --- | --- |
| Max. Diameter of Cloth Roller (mm) | 1200 |
| Cutting Length (mm) | 600-1200 |
| Folding Width (mm) | 20-30 |
| Gross Power (kw) | 6 |
| Max. Cutting Width (mm) | 800 |
| Cutting Precision (mm) | ±4 |
| Production Capacity (pcs/min) | 20-40 |
| Approx. Weight (kg) | 2200 |
| Outline Size (L×W×H)(mm) | 5100×4500×1200 |