SUSTENTAP Consultoria Organic and inorganic fertilizer project

50,000MT/Y compound fertilizer production line

Preliminary proposal

Provide by JSRAT (JIANGSU RIGHT MACHINERY GROUP)

2015/01/06

Equipment list of NPK Fertilizer plant

JIANGSU RIGHT GROUP

SUSTENTAP Consultoria Organic and inorganic fertilizer project

50,000MT/Y compound fertilizer production line

| No | Name | Q’ty | Power （KW） | Remarks | Picture |
| --- | --- | --- | --- | --- | --- |
| W101- W106 W108 | B500 Belt weight | 7 | 7×1.5 | Contain PLC control Capacity: 4-8t/h accuracy: ±0.5% Material:Q235B |  |
| L101#1 | HL250 Bucket elevator | 2 | 5.5×2 | Capacity: 47.2-30m³/h Bucket running speed: 1.5m/s Transmission direction: right Material: Q235B |  |
| M101 | LF600 Cage miller | 2 | 16.5×2 | Production capacity:5-10t/h Final grain: <1mm90% Motor power: 11/7.5kw |  |
| L103#2 | B650 Belt conveyor | 1 | 5.5 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| L102#1 | B650 Belt conveyor | 1 | 4 | Capacity≥5 m³/h Speed of belt: 0.8m/s Journey: 500mm Gauge: 1000mm |  |
| L104#3 | B650 Belt conveyor | 1 | 5.5 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| L105#4 | B650 Belt conveyor | 1 | 7.5 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| M102 | Ø1.8×7m Revolving drum granulator | 1 | 15 | Wall thickness: δ=12 Production capacity: 10t/h Rotational speed of cylinder: 11.5r/min Reducer model: ZQ650 Material: Q235B PVC |  |
| L106#5 | B650 belt conveyor | 1 | 5.5 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| M103 | Ø2.2×22m Dryer 1# | 1 | 37 | Wall thickness: δ=16 Production capacity: 8-14t/h Rotational speed of cylinder: 3.29r/min Reducer model: ZL65 Material: Q235B |  |
| C101 | W4-68No8C Hot air fan | 1 | 18.5 | Pressure: 2177-1481pa Blowing rate: 16985-30134m3/h Material: CS+SS |  |
| C105 | FRP4-72No.4.5A Draught fan | 1 | 7.5 | Pressure: 2554-1673 Blowingrate:5712-10560m3/h Material: FRP+SS |  |
| B101 | Combustion furnace | 1 |  | Coal Furnace 5000Kcal/kg supply of steel parts and fan |  |
| S101#1 | Ø1800 Cyclone | 1 |  | Material: Q235B |  |
| L107#6 | B650 Belt conveyor | 1 | 4 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| L108#2 | HL400 Bucket elevator | 1 | 11 | Capacity: 47.2-30m³/h Bucket running speed: 1.5m/s Material: Q235B |  |
| M104 | Ø1.8×16m Dryer2# | 1 | 18.5 | Wall thickness: δ=14 Production capacity: 5-7t/h Rotational speed of cylinder: 3r/min Reducer model: ZQ650 Material: Q235B |  |
| S102#2 | Ø2000 Cyclone | 1 |  | Material: Q235B |  |
| B102 | Combustion furnace | 1 |  | Coal furnace 5000kcal/kg supply of steel parts and fan |  |
| L109#7 | B650 Belt conveyor | 1 | 3 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| L110#3 | HL400 Bucket elevator | 1 | 7.5 | Capacity: 47.2-30m³/h Bucket running speed: 1.5m/s Material: Q235B |  |
| M105 | Ø1.5×6m Rotary sieve | 1 | 11 | Production capacity: 8-10t/h Rotational speed of cylinder: 17r/min Level: 1 Material: Q235B |  |
| M106 | LP700 Vertical crusher | 1 | 22 | Material: Q235B |  |
| L112#9 | B500 Belt conveyor | 1 | 3 | Capacity≥5 m³/h Speed of belt: 0.8m/s Journey: 500mm Gauge: 1000mm |  |
| L113#4 | HL400 Bucket elevator | 1 | 11 | Capacity:47.2-30m³/h Bucket running speed: 1.5m/s Transmission direction: right Material: Q235B |  |
| M107 | Ø1.8×16m Cooler | 1 | 18.5 | Wall thickness: δ=14 Production capacity: 5-7t/h Rotational speed of cylinder: 3r/min Reducer model: ZQ650 Material: Q235B |  |
| S103 | Ø1800 Cyclone | 1 |  | Material:Q235B |  |
| L114#5 | HL400 Bucket elevator | 1 | 11 | Capacity: 47.2-30m³/h Bucket running speed: 1.5m/s Material: Q235B |  |
| L117#6 | HL400 Bucket elevator | 1 | 11 | Capacity: 47.2-30m³/h Bucket running speed: 1.5m/s Material: Q235B |  |
| L118#7 | HL400 Bucket elevator | 1 | 11 | Capacity: 47.2-30m³/h Bucket running speed: 1.5m/s Material: Q235B |  |
| M108 | ZDS1450 Vibrating screen | 1 | 2.2X2 | Production capacity: 8-10t/h Frequency: 960/min Motor: ZG618-2.2 Material: Q235B |  |
| M109 | Ø1.4×4m Coating machine | 1 | 11 | Wall thickness: δ=12 Production capacity: 8t/h Rotational speed of cylinder: 15.05r/min Reducer model: JZQ500 Material: Q235B |  |
|  | ￠1000 Coating Melting tank |  |  | Weight pump BLDY15-35 |  |
| L115#10 | B500 Belt conveyor | 1 | 3 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| L116#11 | B650 Belt conveyor | 1 | 5.5 | Capacity≥8 m³/h Speed of belt: 0.8m/s Journey: 600mm Gauge: 1200mm |  |
| WL106 WL107 V101 | Automatic packaging unit Include the Packing Weight belt Final Product Hoper | 1 | 3 | Stainless steel Material: SS304 LCS-50-I F710 |  |
| L111#8 | B500 Belt conveyor | 1 | 5.5 | Capacity≥5 m³/h Speed of belt: 0.8m/s Journey: 500mm Gauge: 1000mm |  |
| C102 | G4-68-No10D 1# Dryer Fans | 1 | 55 | Draught fan pressure: 3403-2315pa Blowing rate: 33173-58856m3/h |  |
| C104 | G4-68No9D Cooler Fans | 1 | 30 | Draught fan Pressure: 2756-1873pa Blowing Rate: 24183-42906m3/h |  |
| C103 | G4-68No9D 2# Dryer Fans | 1 | 30 | Draught fan Pressure: 2756-1873pa Blowing Rate: 24183-42906m3/h |  |
| T101 | Ø2×3m Scrubber + chimney | 1 |  | Water circulating system FRP |  |
|  | Urea Melting System | 1 |  | R101 Tank R102 Tank Include pump 1Cr18Ni9Ti |  |
| S104 | Gravity settling chamber 1# for Dryer1 |  |  | 15m×4.5m×8m |  |
| S105 | Gravity settling chamber 2# for Dryer 2 |  |  | 15m×4.5m×8m |  |
| S106 | Gravity settling chamber 2# for Dryer 3 |  |  | 15m×4.5m×8m |  |
| S107 | Exhaust sink |  |  | 8m×5m×3m |  |
|  | Steam boiler | 1 | 2ton 13MPa | Fuel material confirm by buyer later |  |
|  | Electrical control system Operating floor, electric control cabinet, temperature control cabinet and cable |  |  |  |  |
|  | Un-standard parts |  |  | Duct, elbow, ladder stand, platform and son on (30t) |  |
|  | Design fee and know-how fee |  |  |  |  |
|  | Packing, commodity inspection and domestic transportation |  |  |  |  |
|  | Sea freight |  |  |  | After confirm |

Spare parts list for the 1years operation

JSRAT will provide spare parts list in the details design

A.  Commercial proposal

Price schedule for engineering scope of work

According to the result of negotiations to decided.

Price schedule for NPK Fertilizer plant equipment

¥ 4,4300,000 RMB (estimate)

Price for supervision

Calculated as man/day, it can be talk about in the negotiations.

Price for training

$100 per each engineer a day, it can be talk about in the negotiations.

Price for building projects

According to the result of negotiations to decided.

Term of payment

30% down payment

The rest of the progress payments

Equipment delivery must to pay 95%

After the commissioning pay last 5%

Guarantee

JSRAT warranty period is twelve (12) months after the date of running.

JSRAT will continue to provide technical support to ensure the normal operation of equipment.

And other guarantee we will in-depth consultation in the negotiations.

Note:

This proposal is the Preliminary proposal, for business negotiations between the two sides use. It will be negotiated in details during Delegations meeting in china to finalize.