泉州市南侨筑路机械有限公司

NAN QIAO ROAD CONSTRUCTION MACHINERY CO.LTD

地址:福建省泉州市紫帽工业区  邮编Post Code:362213

Address：Zimao industrial park, Jinjiang,Quanzhou,Fujian Province.

Tel：86-595-85954008 85953648 Fax: 86-595-85954618  www.nqc.cn nq@nqc.cn

SALES OFFER

报价表

Quotation date: Jan 14, 2015

报价日期:2015年1月15日

Quotation No. NQC1501151

报价编号:NQC1501151

ONE UNIT OF QLB-1000 Asphalt Mixing Equipment

一套QLB-1000沥青混凝土搅拌站设备

CUSTOMER：

地址(Address)：

电话(Tel)：

电子邮箱(E-mail)：

ATTENTION：

呈：

QUOTED BY: NAN QIAO CO. LTD

报价人：南侨公司

Dear Sir or Madam:

Thank you for your enquiry. We are pleased to submit the following quotation.

非常感谢您的询价，我们很高兴提供下述报价。

Unless otherwise stated, our quotation on this offer sheet is given without engagement.

除另有说明者外，该报价单上的报盘是不受约束的。

- SCOPE OF QUOTATION 报价范围

The scope of quotation of the QLB-1000 Asphalt Mixing Equipment is included in Appendix Ⅰ of this quotation. Modification in connection with technical progress reserved.

附表一是QLB-1000沥青混凝土搅拌站设备报价范围。鉴于技术进步，保留更新的权力。

- WARRANTY 提保

We offer a warranty period of 13 months from the date of dispatch (FOB) from Quan Zhou against faulty material components or workmanship for the supplied goods. Provided the equipment has been operated and maintained in accordance with the operating and instruction manuals. The warranty is limited to the replacement cost of the defective component.  Wear parts are excluded in the warranty.

我们提供从出厂日起13个月的质量担保，包括材料，零件和加工工艺缺失。不按设备操作和维护保养手册规定操作和维护而引起的任何损坏,不在担保范围内。本担保只提供更换损坏的零件。易损件不在保修范围内。

- DATE OF DELIVERY 供货期

The goods will be ready for delivery within 45 working days ex-works, Quan Zhou, after technical clarification and receipt of firm order, as well as down payment and L/C, whichever is later, has been received. The date is subjected to confirmation on receipt of the order.

在收到正式订单和技术确认以及订金和信用证后45个工作日内设备在泉州准备好发运。具体日期在收到订货时确认。

- PRICE 价格

The total price for the scope of supply as shown in AppendixⅠof this quotation is:

| 序号NO. | 设备 DESCRIPTION | 人民币 RMB | 备注 MARK |
| --- | --- | --- | --- |
| 1 | 主机Main Machine | 105,0000 | 出厂含税价 |

- TERMS OF PAYMENT 付款条件

30% down payment by T/T;

30% 定金电汇支付

70% Paid before shipment.

70%发货前付清。

- VALIDITY有效期

This quotation will be valid for 50 days from the date of quotation stated on the covering letter.

本报价自封面日期起50天内有效。

APPENDIX Ⅰ附件一

- 主要技术性能参数Main technical parameters

  - 生产能力：60-80t/h（ 标准工况下）

Capacity: 60-80t/h (under standard working condition)

  - 生产适用范围：粗粒式、中粒式、细粒式、砂粒式。

APPLICATIONS: coarse grain bitumen mixture, medium-grain bitumen mixture, fine grain bitumen mixture and sand grain bitumen mixture。

  - 矿料计量精确度：±0.5%

Aggregate weighing accuracy: ±0.5%

  - 沥青计量精确度：±0.25%

Bitumen weighing accuracy: ±0.25%

  - 粉料计量精确度：±0.30%

Filler weighing accuracy: ±0.30%

  - 成品料温度：140-160（最高可达180℃），可调

Hot material temperature: 140-160( up to 180℃), adjustable

  - 成品料温度稳定性：±5℃

Stability of hot material temperature: ±5℃

  - 燃油消耗率：在燃油热值为46055kj/kg、标准工况下

Fuel consumption: based on the fuel calorific value=46055kj/kg, and under standard working condition:

    - 当骨料含水率：≤3%时，耗油量5kg/吨成品料

Aggregate moisture:≤3%, 5kg per ton hot mixed product.

    - 当骨料含水率：≤5%时，耗油量6kg/吨成品料

Aggregate moisture:≤5%,6kg per hot mixed product

    - 当骨料含水率：≤7%时，耗油量6.5kg/吨成品料

Aggregate moisture:≤7%,6.5kg per hot mixed product.

  - 筛分效率：≥95%，能满足各种沥青混合料级配要求，能剔除大骨料。

Screening efficiency:≥95%, can satisfy the demands of various kinds of bituminous mixtures and eliminate large aggregates.

  - 搅拌周期：40-60秒，任意设定。

Mixing cycle time: 40-60s, set up freely

  - 除尘效果：使用布袋式除尘器时，排放粉尘浓度≤100mg/Nm3，林格曼黑度≤1级。

Dust removing efficiency: dust emission level≤100mg/Nm3

  - 配套总功率：255KW

General power consumption:       244Kw

  - 控制方式：全自动操控，半自动、手动操作备用。

Controlling mode: full automatic operation, semi-automatic、manual operating for option.

  - 成品料卸料高度：3200mm×3670mm(高×宽)

Hot material discharging height: 3200mm×3670mm(height×width)

  - 整机外型安装场地尺寸：最大长度为40m，最大宽度为30m。

Overall dimension: maximum height 40m, maximum width 30m.

Notes: Relating to Plant Capacity 与生产能力有关的条件：

- The average moisture content is for surface moisture only.

平均含水量只是指材料表面的含水量，材料内部的含水量将会降低干燥筒的生产能力

2	Ambient temperature taken as 15ºC.

周围的大气温度为15℃。

3	Material taken as 1600kg per cu.m.

原材料的重量为1,600 公斤/ 立方米。

4	Capacities include filler and bitumen.

产量包括石粉和沥青重量。

5	Aggregate feed to plant is in correct proportion required for mix specifications.

进入拌和机的骨料比例要正确，要符合级配的规范。

6	Filler density 1120kg per cu.m.

石粉的密度为1,120 公斤/ 立方米。

7	Aggregate is non-porous and not excessively flaky.

骨料不能是疏松多孔和片状的。

8	Altitude 150m above sea level.

海拔150米

2、QLB-1000沥青混凝土搅拌站设备组成:

QLB-1000  Asphalt Mixing Equipment Consists of:

| 序号No. | 名称 Description | 规格Specification | 数量QTY. | 备注 Notes |
| --- | --- | --- | --- | --- |
| 1 | 配料站 COLD FEEDER | 骨料仓 Aggregate hoppers | 容量8m3 CAPACITY 8m3 | 4 |  |
|  |  | 给料机输送能力 Capacity of feeder conveyor | 0-50t/h |  |  |
|  |  | 减速机 Gear box | BWY18-29-2.2 | 4 |  |
|  |  | 输送皮带 Belt conveyor | B500×2500×10 | 4 |  |
| 2 | 水平皮带输送机(集料皮带机) COLLECTING CONVEYOR | 最大输送量 Capacity | 100T/h |  |  |
|  |  | 电动滚筒 Electric drum | DT4-1.25-320X650 |  |  |
|  |  | 输送皮带 Belt conveyor | B650×25000×10 | 1 |  |
|  |  | 清扫器 Cleaner |  |  |  |
| 3 | 倾斜皮带输送机 INCLINED BELT CONVEYER | 最大输送量 Maximum capacity | 100T/h |  |  |
|  |  | 电动滚筒 Electric drum | YDT4-1.25-320X500 | 1 |  |
|  |  | 输送皮带 Belt conveyor | B500×18000×10 | 1 |  |
|  |  | 集料斗 Material collecting hopper |  | 1 |  |
|  |  | 清扫器 Cleaner |  |  |  |
| 4 | 烘干滚筒 ROTARY DRYER | 支架、托轮轴承座等 Support, support roller, bearing etc. |  | 1 |  |
|  |  | 烘干筒体 Dryer drum | φ1600mm×6480mm | 1 |  |
|  |  | 石料最大烘干能力 Capacity | 100T/h（石料含水率moisture≤5%） |  |  |
|  |  | 减速机 Geared motor | BWY27-29-7.5KW | 4 |  |
|  |  | 测温仪 Thermostat |  | 1 |  |
| 5 | 主燃烧器（燃油）BURNER(OIL) | 燃烧器 Burner |  | 1 |  |
|  |  | 燃油种类 Fuel type | 重油 Heavy oil |  |  |
|  |  | 标准耗油量 Fuel consumption | 7～8kg/t （重油heavy oil） |  |  |
|  |  | 电机功率 Motor | 15Kw | 1 |  |
| 6 | 一级旋风除尘装置 PRIMARY DUST COLLECTION | 旋风除尘器 Cyclone dust separator |  | 1 |  |
|  |  | 旋风管数量 Cyclone tubes |  | 2 |  |
|  |  | 旋风管直径 Cyclone tube diameter | 900mm |  |  |
|  |  | Φ219螺旋输送机 Φ219 Screw conveyor | BWY22-23-4KW | 1 |  |
| 7 | 热料提升机 HOT AGGREGATE ELEVATOR | 型式 Type | 锚链式 Anchor chain |  |  |
|  |  | 最大提升机能力 Capacity | 100t/h |  |  |
|  |  | 减速机 Gear box | BWY27-17-7.5Kw | 1 |  |
| 8 | 粉料提升机 POWDER ELEVATOR | 型式 Type | 锚链式 Anchor chain |  |  |
|  |  | 最大提升能力 Capacity | 20 ton/hour |  |  |
|  |  | 减速机 Gear box | BWY18-17-4Kw | 1 |  |
| 9 | 筛分设备 VIBRATING SCREEN | 型式 Type | 四层式（粗、中、细、砂）筛分效率≥95％ Four deck to give four sizes plus rejects, efficiency up to 95%。 | 1 |  |
|  |  | 驱动电机功率 Drive | 5.5KW | 1 |  |
|  |  | 激振器 Vibration exciter |  | 1 |  |
| 10 | 粉料供给系统POWDER FEEDING SYSTEM | Φ219螺旋输送机（减速机功率） Φ219 screw conveyor | BWY22-23-4KW | 1 |  |
|  |  | 输送能力 Capacity | 25t/h |  |  |
|  |  | 粉仓容量 Filler Hopper capacity | 2Ton | 1 |  |
| 11 | 中间热料仓 INTERIM HOT STONE BIN | 热料仓数量 Bin quantity |  | 4 |  |
|  |  | 热料仓总容量 Bin total capacity | 15m3 |  |  |
|  |  | 气缸 Air cylinder | QGBES80×200-L3 | 4 |  |
|  |  | 观察孔 Observation hole |  | 4 |  |
| 12 | 楼体机架 STEEL FRAME WORK OF MIXING PLANT | 拌和楼立于钢框架结构上，有人行道和安全保护装置 Mixing tower on steel framework with access safeguard. |  | 1 |  |
|  |  | 接卸料通道 Discharge passageway |  |  |  |
|  |  | 净空间 Net space | 高3000mm×宽3600mm H3000mm×W3600mm |  |  |
| 13 | 称量系统 WEIGHING SYSTEM | 砂石料计量斗容量 Sand and stone weighing hopper | 1500kg | 1 |  |
|  |  | 计量精度 Weighing accuracy | ±0.5% |  |  |
|  |  | 传感器 Load cell | HL-S8-500 | 3 |  |
|  |  | 气缸 Air cylinder | QGBES125X250-L3 | 1 |  |
|  |  | 粉料计量斗容量 Filler weighing hopper | 300kg | 1 |  |
|  |  | 计量精度 Accuracy | ±0.3% |  |  |
|  |  | 气缸 Air cylinder | QGBES80X100-L3 | 1 |  |
|  |  | 沥青计量斗容量 Bitumen weigh tank capacity | 200kg | 1 |  |
|  |  | 计量精度 Weigh accuracy | ±0.25% |  |  |
|  |  | 气缸 Air cylinder | QGBES80X100-L3 | 1 |  |
|  |  | 传感器 Load cell | HL-S8-100 | 6 |  |
|  |  | 沥青泵（2寸） Bitumen pump (2inch) | 5.5KW | 1 |  |
|  |  | 沥青泵能力 capacity | 15m3/h |  |  |
|  |  | 沥青三通阀（2寸） Bitumen T-valve (2inch) |  | 1 |  |
|  |  | 三通阀气缸 T-valve air cylinder | QGBES80X160-L3 | 1 |  |
| 14 | 浆式搅拌器 PADDLE MIXER | 搅拌器容量 Mixer capacity | 1000kg |  |  |
|  |  | 搅拌周期 Mixing cycle | 0:00:45 |  |  |
|  |  | 搅拌型式 Mixer type | 双卧轴强制搅拌 Double-horizontal shaft forced mixer |  |  |
|  |  | 减速机 Gear box | ZQ650-23.34-Ⅰ | 1 |  |
|  |  | 放料门型式 Discharge door type | 翻转式 Tilting |  |  |
|  |  | 气缸 Air cylinder | QGBES160X630-L3 | 1 |  |
|  |  | 电机功率 Motor power | 37 KW |  |  |
|  |  | 空压机 Air compressor | 7.5KW | 1 |  |
|  |  | 储气罐 Air tank | 0.25 M3 | 1 |  |
| 15 | 导热油加热沥青设备 HOT OIL HEATING BITUMEN EQUIPMENT | 有机热载体炉 Hot oil heat transfer heater | YYW-450Y（燃油） | 1 |  |
|  |  | 燃烧器（柴油） Burner (diesel oil) |  | 1 |  |
|  |  | 有机热载体炉发热量 Hot oil heat transfer heater calorific capacity | 40万大卡 400,000 kilocalorie |  |  |
|  |  | 导热油泵 Hot oil pump | DRB80-50 7.5KW | 1 |  |
|  |  | 高低位油槽及铁塔 High position tank and low position tank with steel frame work. |  | 1 |  |
|  |  | 电缆线 Cable |  | 1 |  |
|  |  | 电气控制操作柜 Control panel |  | 1 |  |
|  |  | 燃油加热储罐容量 Fuel heating tank capacity | 30吨 ton | 1 |  |
| 16 | 沥青供给系统BITUMEN FEEDING SYSTEM | 沥青泵（2寸） Bitumen pump (2inch) | 5.5KW | 1 |  |
|  |  | 沥青泵能力 Bitumen pump capacity | 15m3/h |  |  |
|  |  | 沥青保温方式 Bitumen tank insulation | 导热油管道伴热+岩棉 Hot oil pipe with mineral wool |  |  |
|  |  | 沥青卸油脱水池 Bitumen discharge tank | 3吨 ton | 1 |  |
|  |  | 沥青保温储罐 Bitumen tank with insulation | 30吨 ton | 2 |  |
| 17 | 电器控制系统CONTROL SYSTEM | 控制形式 Control mode | 自动、手动任意切换 Man/Auto |  |  |
|  |  | 工控机 Industrial computer |  | 1 |  |
|  |  | 强电柜 Power cabinet | 电源电压380V Power 380V 50Hz | 1 |  |
|  |  | 弱电柜 Control cabinet | 控制电压220V Control system voltage | 1 |  |
|  |  | 按钮, 接触器, 热继电器, 中间继电器等 Buttons, contacts, thermo relays, relays etc |  | 1 |  |
|  |  | 可编程控制器 PLC | PLC模块 | 1 |  |
|  |  | 变频器 Invertor | 韩国LG | 4 |  |
|  |  | 打印机 Printer | EPSON | 1 |  |
|  |  | UPS电源 UPS | 500W | 1 |  |
|  |  | 组态软件 Control soft |  | 1 |  |
|  |  | 操作界面 Touch screen | 触摸屏5.7″ | 1 |  |
|  |  | 操作界面 Display | 17″彩显 | 1 |  |
| 18 | 操作室 CONTROL ROOM | 外形尺寸 dimension | 长3800×宽2300×高2600mm L3800×W2300×H2600mm | 1 |  |
|  |  | 材料 Material | 阻燃装饰板+保温层+彩钢板 Insulated color steel panels |  |  |
|  |  | 空调 Air conditioner | 1.5匹分体式 1.5 HP | 1 |  |
|  |  | 人民币价格price：20000 |

布袋除尘 Bag Filter

| 二级大气反吹袋式除尘SECONDARY BAG FILTER | 过滤面积 | 390m2 |  |  |
| --- | --- | --- | --- | --- |
|  | FILTRATE AREA |  |  |  |
|  | 滤袋数量 Bags quantity | 杜邦布袋 DuPont Normex | 320 |  |
|  | 引风机风量 Fan capacity | 36140 m3/h |  |  |
|  | 粉尘排放浓度 Dust emission | ≤100mg/Nm3 |  |  |
|  | 引风机功率 Fan power | 45 KW |  |  |
|  | 排废、排尘减速机 Geared motor for dust emission | BWY22-43-4KW |  |  |
|  | Φ219螺旋输送机 Φ219 Screw conveyor | BWY22-23-4KW | 1 |  |
|  | 空压机 Air compressor | 7.5KW | 1 |  |

水除尘 Wet Dedusting System

| 水除尘 WATER DEDUSTING SYSTEM | 水除尘器 DEDUSTER |  | 1 | 套SET |
| --- | --- | --- | --- | --- |
|  | 引风机功率 FAN POWER | 45 Kw | 1 | 台SET |
|  | 潜水泵 UNDERWATER PUMP | 2.2KW | 1 | 台SET |

附件二: 备品备件清单

APPENDIX Ⅱ: SPARE PART LIST

| 序号 No. | 配件名称 Description | 件号规格 specification | 数量 Quantity |
| --- | --- | --- | --- |
| 1 | 搅拌叶片A Paddle A for mixer | 1000-01 | 1 |
| 2 | 搅拌叶片B Paddle B for mixer | 1000-02 | 1 |
| 3 | 侧衬板A Side liner A for mixer | 1000-03 | 1 |
| 4 | 侧衬板B Side liner B for mixer | 1000-04 | 1 |
| 5 | 弧衬板A Arc liner A for mixer | 1000-05 | 1 |
| 6 | 弧衬板B Arc liner B for mixer | 1000-06 | 1 |
| 7 | 弧衬板C Arc liner C for mixer | 1000-07 | 1 |
| 8 | 搅拌臂A Mixing Arm A for mixer | 1000-08 | 1 |
| 9 | 搅拌臂B Mixing Arm B for mixer | 1000-09 | 1 |
| 10 | 气缸密封件 Sealing for air cylinder | QGB125 | 2 |
| 11 | 气缸密封件 Sealing for air cylinder | QGB80 | 5 |
| 12 | 气缸密封件 Sealing for air cylinder | QGB63 | 1 |
| 13 | 电磁阀换向阀 Solenoid valve | Q25DC-L15 | 2 |
| 14 | 上托辊（1） Upper support roller (1) | Φ89 | 2 |
| 15 | 上托辊（2） Upper support roller (2) | Φ89 | 2 |
| 16 | 挡边托辊 Flange support roller | Φ89 | 2 |
| 17 | 除尘布袋 Bags for bag filter |  | 5 |
| 18 | PVC气管 PVC air tube | Φ12×1 | 30 |
| 19 | 按钮开关 Button and switch |  | 2 |

EXCLUSIONS

不包括

- Civil works, but provide loading drawing.基础工程，但我们提供基础图

- Any power source.任何电源

- Link cables between generating set and our motor control panel and essential services panel.接到我们控制室的电源进线

- Any item not definitely specified.任何本报价未提及的项目

Installation

# 安装 调试

- 卖方负责到最终用户工地安装调试本设备，买方负责卖方工程技术人员国外的费用，包括食宿和交通费用。技术人员工资为400RMB/天，由买方支付。

The Seller shall send engineers to End User building site to install the plant. The buyer shall bear all cost for seller’s engineers at abroad including return airfare, accommodation, meals and local transport. The Buyer should pay Seller technician wage 400Yuan RMB (Equal to 60 US Dollars) per day。

- 设备安装调试时，我们工程师对用户进行机械，电工，和维修保养方面的知识进行培训。

During plant installation and commissioning our engineer will undertake site training of customer's mechanical, electrical and maintenance personnel.

- 设备安装调试时，用户提供所有的配合人员、翻译、起重设备及必须的原辅材料。

During plant installation and commissioning Customer to provide all skilled and unskilled site labor，interpreter, cranage and necessary auxiliary material.

# VOLTAGE

# 电压

380 Volts 3 Phase 50 hertz. 电压——380伏，3相，50赫兹

Illuminate to be 220volt,50 hertz. 照明：电压220伏

MANUALS

说明书

We include for two sets of "Operators and Maintenance Instruction Manuals" and "Illustrated Spare Parts Manuals" in the English and Mandarin Chinese Languages.

我们提供二套英文和中文版的完整的《操作维修手册》和《备件手册》。

# # # #