Automatic Hamburger Production Line (LTHP-100) (two pages)

No matter meat, seafood, poultry or vegetable, the production line can fulfill the processing procedure of forming, preduster (flavor), battering, breading etc. The equipment can be connected to the fryer, cooking apparatuses, instant freezer and packing machine to match a full automatic processing line to produce several of popular foodstuffs. The raw materials that it can use include pork, beef, chicken, fish, onion, potato and so on.

This production line includes the following machines (Capacity: 2100pcs burgers per hour):

| No. | Item | Function | Parameter | Unit Price (USD) |
| --- | --- | --- | --- | --- |
| 1 | Hamburger Former | Forming the meat into various shapes and sticking a paper under the Hamburger | Power: 0.55kw, Tank Capacity: 30L Production capacity: about 2100pcs/hour Thickness of product: 8-15mm Maximum diameter: 100mm (for round burger ) Overall dimension: 860×600×1400mm | 4,200 |
| 2 | Battering Machine | Covering Batter(flour paste) on hamburger | Width of the belt: 200mm Power: 0.55kw, Input height: 690mm, Output height: 770—620mm Over dimension: 1400×550×1250mm | 3,800 |
| 3 | Breading Machine | Covering Bread crumb on the hamburger | Belt: 200mm, Input height: 700mm Output height: 810-660mm, Power: 0.86kw Overall dimension: 1720×650×1400mm | 5,700 |
| 4 | Continuous Fryer Model 200 | Frying Foods in continuous system and ensure the whole line under full automatic | Full-automatic complying with the whole line, Power: 30kw | 7,500 |
| Total Price | FOBQingdao USD21,200 |

Machines: From right to left: forming(battering(breading(frying

# Text boxes

Batch Fryer