Automatic Hamburger Production Line (LTCH-100) (3 pages)

No matter meat, seafood, poultry or vegetable, the production line can fulfill the processing procedure of forming, preduster (flavor), battering, breading, frying etc. The equipment can be connected to the fryer, cooking apparatuses, instant freezer and packing machine to match a full automatic processing line to produce several of popular foodstuffs. The raw materials that it can use include pork, beef, chicken, fish, onion, potato and so on. In addition, these machines can produce high quality diversified patterns pet food. This production line includes the following machines:

| No. | Item | Function | Parameter | Unit Price (USD) |
| --- | --- | --- | --- | --- |
| 1 | Meat Grinder LTJR-40 | Used to grind any kind of boneless meat | Capacity: 300-400kg/hour Size of minced meat: 5-30mm(adjustable) Power: 3kw; Speed of Screw: 417r/min | 3,800 |
| 2 | Meat Mixer LTJB-100 | Mixing various sizes of meat with other flavors or materials | Capacity: 75 kg/time; Volume of Bin: 100L; Power: 1.5kw; Mixing Speed: 75r/min; Dimensions: 1300*530*990mm | 3,500 |
| 3 | Burger Former Model 100 | Forming the meat into various shapes | Power: 0.55kw, Tank Capacity: 30L Production capacity: about 2100pcs/hour Thickness of product: 8-15mm Maximum diameter: 100mm (for round burger) Overall dimension: 860×600×1400mm | 4,200 |
| 4 | Freezer | Freezing the meat processing food, such as meat patty, chicken nugets, burger etc. | Dimension: 1810x800x2000mm Temperature:-15℃~-22℃;Power:220v/50hz,991w Temperature: - 15 ℃ ~ - 22 ℃, Power: 220V / 50Hz, 1000 W Volume:1800L Mode of refrigeration:Air cooling and frostless Features:1.Famous closed compressor with low noise and power consumption 2.Embedded System of all-digital temperature control, easy adjustable and stable performance 3.Full stainless steel,novel style. Plate:400x600mm | 3,800x4 |
| Total Price | FOBQingdaoUSD26,700 |

For Hamburgers: (from right to left)Grinding(Mixing(Forming( Battering(Breading(Frying are needed.

Payment Term: 100%T/T

Guarantee: one year after installation. If there is any breakdown caused not by misoperation reason, we would send free new parts.

Lead Time: 30 days after receiving of advance payment.

Packing: standard seaworthy export packing.

-------------------------------------------------------------------------------------

Melody Tang

Tel: 0086-531-86398889; Mobile: 18764157970

Skype: melody.tang7; Email:trade@znmachinery.com

Website:http://www.foodmachinerychina.com