Automatic Chicken Nuggets Production Line (LTNP-100)

No matter meat, seafood, poultry or vegetable, the production line can fulfill the processing procedure of forming, preduster (flavor), battering, breading etc. The equipment can be connected to the fryer, cooking apparatuses, instant freezer and packing machine to match a full automatic processing line to produce several of popular foodstuffs. The raw materials that it can use include pork, beef, chicken, fish, onion, potato and so on. In addition, these machines can produce high quality diversified patterns pet food.

This production line includes the following machines: (Capacity: 50-100kg/hour)

Equipment List and Description:

| No. | Item | Function | Parameter | Unit Price (USD) |
| --- | --- | --- | --- | --- |
| 1 | Chicken Nuggets Former | Forming the meat into various shapes | Power: 0.55kw, Tank Capacity: 30L Production capacity: about 2100pcs/hour Thickness of product: 8-15mm Maximum diameter: 100mm (for round burger) Overall dimension: 860×600×1400mm | 4,200 |
| 2 | Battering Machine | Coating Batter(flour paste) on nuggets | Belt width: 200mm, Input height: 690mm Output height: 770—620mm, Power: 0.55kw, Overall dimension: 1380×550×1350mm | 3,800 |
| 3 | Preduster | Coating flour or flavor on nuggets | Belt width: 200mm, Input height: 700mm Output height: 810-660mm, Power: 0.86kw Overall dimension: 1680×580×1400mm | 6,800 |
| 4 | Battering Machine | Coating Batter(tempura) on nuggets | Belt width: 200mm, Input height: 700mm Output height: 810-660mm, Power: 1.16kw Overall dimension: 1700×650×1550mm | 3,800 |
| 5 | Continuous Fryer | Frying Foods according to required temperature and time | Stainless Steel, Power: 30kw, Frying temperature: 170-180℃ Frying time: 20sec-2min, Width of belt: 300mm, Dimension: 2700×789×1344mm | 7,500 |
| Total Price | FOBQingdao USD26,100 |

Machines: From right to left: Forming( Battering(Breading(Predust(Frying

Trade Terms:

Payment Term:30% T/T as advance payment and 70%T/T before shipment

Delivery Time:30days after receiving the downpayment

Packing Method: Film Closed/Wooden Case

Melody Tang

Tel:0086-531-82316905

18764157970;

Skype: melody.tang7

Email:trade@znmachinery.com;

Website:http://www.foodmachinerychina.com