BZB-6300 Prep-station

| Outside Size (mm) | 7150×4000×3430 | Front Door(mm) | No |
| --- | --- | --- | --- |
| Inside Size(mm) | 6400×4000×2650 | Total Power(kw) | 7 |

| Cabin System | 1) Roof construction: cold rolling plate; Roof Panel: galvanized steel 2) Front and Side: PVC rolling curtain,remote control. 3) Back wallboard: EPS steel skin panel, 50mm Thick |
| --- | --- |
| Air Circulation System | 1) Model:YDW-5.6s; Capacity:15000m3/h; Pressure:800Pa; Speed:900rpm, 1 sets,power:5.5KW 2) Fan Cabin: profile framework, Assembly of steel plate cabin; Durable,beautiful and easy for maintenance |
| Purification System | Malti-layer filtering structure,the ceiling filters capture granules bigger than 5μm.The whole purification system has capacity of large volume of dust. |
| Environmental System | DDual filtering structure,the first filter,under the grids,captures bigger granules,the second filter,the fiber glasses filter,under the exhaust cabin,captures the rest granules. |
| Light System | Ceiling Light: 24pcs 36w Philips Lamp; Light can make the room bright and uniformity. Ballasts is professional and durable. |
| Controlling System | It is assembled by good electronic components. Main circuit has Multi-protection. Working Switch, Light Witch, Emergency Stop, Breakdown Alarm. |