改

Website: www.gz-btb.com

8400 Spray booth 6.9m*4m*2.75m

Outside dimension:7000×5550×3470mm（L×W×H）；

Inside dimension: 6900×4000×2800mm（L×W×H）；

Front door dimension: 3000×2700mm（W×H）；

Working door dimension: 800×2000mm（W×H）；

Cabin system:

- Wall panel: 50mm thick flame-resistant and heat-preserving

EPS board; 0.426 thick colored steel.

Roof panel: 0.8mm galvanized sheet;

2) Basement: steel structure base; two line grilles, three diamond plates; height is 300mm; three ramps;

Air circulation system:

| Inhaling Ventilator | Model： YDW-4.5L1 Blower Capacity: 24000m3/h Pressure: 800Pa Rolling Speed: 900rpm Power: 4kw Quantity: 2sets | Exhaust Ventilator | Model:YDW5.6M Capacity:21000m3/h Pressure:800Pa Velocity:900rpm Power:7.5KW Quantity:1Set |
| --- | --- | --- | --- |

Electric dampers actuate from spraying to baking cycle,equip with electric damper for exhaust air.

Generator: back upper intake air,back up extract air,quadrate steel frame,coated steel;

Air purification system: G3 grade, Pockets filter Pre-filter, EU5 / F5 high efficiency filter (ceiling filter), green fiber glass filter / G3 grade floor filter; Pocket filter or M green fiber glass filter and active carbon exhaust fan filter.

Heat system: stainless steel SUS304 heat exchanger, RIELLO G20 diesel burner one stage, heating capacity is 180000Kcal/h, electric damper from spraying to baking cycle; oil consumption 4~6L/set;

Spray to baking switch: 20N Electrical Actuator

Chimney Duct: 4 meters straight ducting and one chimney hood

heating time is 5~7 minutes;

Max heating temperature:80degree;

Lighting system:≥900Lux

Ceiling Lights: 8Groupsx4Pcs=32Pcs x36W ;Side lights:8GroupsX2Pcs=16Pcsx36W;

Glass: all glass is clear tempered glass.

Control box: Lighting switch, spraying, risen-temperature spraying, baking, baking temperature, time setting, failure indicator, temperature controller, emergency stop, breakdown alarm;

Total power: 17.5KW