200 kg per Batch Coffee Bean Roaster

Sampler                                        Temperature Sensor

I．Description

The machine consists of roaster and cyclone husk collector. The cyclone system (dust and husk collector) can collect the dust and shell into its drawer.

II. Features & Advantages

1. The internal cylinder is made of thick cast iron, which helps preserve heat and controls the roasted degree, thus the coffee bean won’t be overheated and burned. The cast iron also helps save energy and reduce the gas usage.

2. The machine is equipped with a viewing window and a sampler. The roasting degree can be observed at any time.

3. The machine provides accurate temperature sensing, and the temperature is displayed on the screen. The baking temperature is easy to regulate.

4. The machine is equipped with automatic ignition and flame-out protection devices.

If the fire is not ignited within 22seconds, the electro magnetic valve will cut the connection between the gas and machine, thus ensure the safety of operation.

5. With a draught fan and a big cooler pan, the coffee beans can be cooled in 1 to 3 minutes. The air from the draught fan will be discharged in other direction and has no effect on the roasted bean.

6. Equipped with a clutch, the machine won’t be damaged when sudden power failure occurred.

7.Our machine has collector which can collect the smoke and scraps caused during the process of roasting, thus keep the environment clean.

8.The handle in the discharge gate is not closed to the gate so as that the heat from roasted coffee won’t harm operator.

9. The machine has an elegant design, easy operation, compact structure and occupies little floor space.

III. Technical Parameters

| Model | 200kg/batch |
| --- | --- |
| Main motor | 3kw |
| Mixing Motor | 3kw |
| Exhausting Fan | 1.5kw |
| Cooling Fan | 6kw |
| Heating mode | LPG/Natural Gas |
| Baking capacity | 200kg/batch |
| Dimension | 6600*2200*3000m |
| Price | FOB QingdaoUSD90,000 |

Payment Term:30%T/T as advance payment and 70% T/T before shipment.

Guarantee: one year after installation.

Lead Time: 30 days after receiving of advance payment.

Packing: standard seaworthy export packing.

---------------------------------------------------------------------------------

Melody Tang

Tel:0086-531-86398889

18764157970

Skype: melody.tang7

Email:trade@znmachinery.com

Website:http://www.foodmachinerychina.com