TECHNICAL DATA OF DIESEL GENERATOR UNIT

I Main technical data of diesel generator柴油发电机组主要参数

1. Code型号: 30GF

2. Rated power额定功率: 30kW

3. Rated voltage额定电压: 400V

4. Rated current额定电流: 54A

5. Rated frequency额定频率: 50Hz

6. Rated power factor额定功率因数: COS=0.8 (lagging)

7. Static voltage adjustment静态电压调整: ≤1%

8. Transient voltage adjustment瞬变电压调整: -15%~ +20%

9. Voltage stabilization duration电压稳定时间: ≤1.5sec

10. Voltage fluctuate电压波动: ≤1.0%

11. Static frequency adjustment静态频率调整: ≤3%

12. Transient frequency adjustment瞬时频率调整: ≤±10%

13. Frequency stabilization duration频率稳定时间: 3sec

14. Frequency fluctuate 频率波动: ≤1%

15. Diesel consumption in full load全额柴油消耗: 206g/kw/h

16. Dimension尺寸: 1650*750*950

17. Weight重量: 650KG

II Technical data of diesel engine柴油机参数

1. Code型号: K4100

2. Type类型: four cycle engine, direct injection, compression ignition四冲程柴油机, 直接喷射, 压缩点火

3. Cooling method冷却方法: pump circulation water cooling system水循环冷却

4. Cylinder type气缸类型: 4 cylinders, upright 4气缸，直立的

5. Drainage排水: 3.6L

6. Lubricant oil volume润滑油体积: 10L

7. Diameter / stroke of cylinder: 气缸直径/ 冲程100mm*115mm

8. Rotating speed转速: 1500r/min

9. Speed adjustment速度调节: mechanical adjustment机械调节

10. Starting method启动方法: DC12V electric start 电启动

III Technical data of generator:发电机参数

1.  Code型号: STC-30KW

2.  Type类型: with brush, AVR automatic voltage adjustment带刷及自动电压调整器

3.  Phase / wiring相电/接线: 3 phase, four wires 3相电，4接线

4.  Insulation grade绝缘等级: H

5.  Protection grade防护等级: IP22

IV Buildup of the generator unit柴油发电机组组成: diesel engine, generator, control panel柴油机，发电机，控制面板。

The control panel is equipped with some indicating meters for voltage, current, frequency and water temperature.

控制面板装有指示仪，指示电压，电流，频率及水温。

V Accessories附件:

Muffler, storage battery and connection wire, damping cushions, tool box, documentation, etc.

消声器，蓄电池和连接的电线，阻尼垫，工具箱及文件材料。