Recycling Granulator

It's used for processing old woven bag, plastic film or other broken old plastic to make them into granules that will be reused as raw materials.

| Model No. | SJ-FL120-II |
| --- | --- |
| Diameter of Screw (mm) | 120 |
| L/D Ratio of Screw | Main Screw:10:1 |
| Rotational of Speed Screw (r/min) | 50-80 |
| Power of Motor (kw) | 18.5 |
| Power of Sub-motor (kw) | 7.5 |
| Motor Power of Grain Cutting (kw) | 1.1 |
| Heating Power (kw) | 12 |
| Production Capacity (kg/h) | 40-80 |
| Overall Dimensions (L×W×H) (mm) | 4500×2000×1100 |
| Approx. Weight (kg) | 1200 |
| Price (FOB WENZHOU) | USD 7250.00 |

Plastic Crusher

Waste tape, rejected products and scrap in the process of woven bags can be used as material for tape drawing again after being crushed by the machine.

| Model No. | YFP-300 | YFP-500 |
| --- | --- | --- |
| Capacity (kg/h) | 100 | 200 |
| Width of Blade (mm) | 300 | 250×2 |
| Power of Motor (kw) | 7.5 | 11 |
| Approx. Weight (kg) | 400 | 600 |
| Installing Dimensions (L×W×H) (mm) | 1050×800×1370 | 1300×1100×1600 |
| FOB Wenzhou Price | USD1350.00 | USD1850.00 |

Remarks:

Country of supply/origin: China

Type of packing: Packed in nude

Warranty Period: One year from the shipment date except quick-wear parts.

Term of payment: 30%T/T as the advance, 70%T/T before the delivery or 100% by irrevocable L/C at sight

Delivery period: Within 35 days after we receive the advance payment or L/C

Installation: The buyer provide each technician the accommodation, the round-trip ticket, visa and salary $65/person/day.