Full-automatic baler

This series machine mainly is used for baling cartons, cotton yarn, plastic, wood, etc. It is designed as horizontal structure, hydraulic transmission, electrical control. Usually the pressure force of this series is from 50 ton to 125 ton, the efficiency is higher than the vertical structure. Also, we can produce the machine as manual binding or automatic binding according to the requirement.

Features:

PLC controlled, combined with touch screen $ visible window, real-time diagram of movements & alarm. Size of bale can be set on touch screen.

- Design of floating neck movable on 3 sides (left, right & up), good for distribution of pressure on 4 sides, suitable for baling of different materials.

- Automatic belting to increase speed of baling.

- Spherical connection between pushing cylinder & ram to ensure reliability & life of seals in cylinder.

- Dispersed cutting blades used on feeding opening to ensure high efficiency.

- Design of low-noise hydraulic circuit with high efficiency & low trouble rate.

# Products model and technique list

| Model | Hydraulic power | Packing size | Feed opening size | Bale density | Bale line | capacity | Bale wire | Power | Machine weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MA40-7272 | 40ton | 720*720*300-1600mm | 1000*660 mm | 300kg/m3 | 4line | 1-3T/h | ∮2.5*4 PCS | 18-22kw/34-30HP | 8ton |
| MA60-7575 | 60Ton | 750*750*300-1800mm | 1200*690 mm | 350Kg/m3 | 4Line | 2-4T/h | ∮2.5*4 PCS | 22-30KW/30-40HP | About 10Ton |
| MA80-110 80 | 80ton | 1100*800*300- 2000mm | 2000*760 mm | 400Kg/m3 | 4Line | 4-7T/h | ∮2.8*4 PCS | 30-45KW/40-60HP | About 13Ton |
| MA100-110110 | 100ton | 1100*1100*300- 2100mm | 1800*1000mm | 500Kg/m3 | 5Line | 6-8T/h | ∮2.5*5 PCS | 45-60KW/60-80HP | About 17Ton |
| MA120-110110 | 120ton | 1100*1100*300- 2100mm | 2000*1060mm | 550Kg/m3 | 5Line | 8-10T/h | ∮3.0*5 PCS | 60-75KW/80-100HP | About 20Ton |
| MA160-110110 | 160Ton | 1100*1100*300- 2100mm | 2400*1060mm | 600Kg/m3 | 5Line | 12-15T/h | ∮3.2*5 PCS | 75-90KW/100-120HP | About 23Ton |