ABOUT US

- COMPANY INTRODUCTION

Founded in the early 1980s as one of the few state-authorized packing machinery enterprises, and re-founded as a private company in 2000. Shanghai Zhonghe Packing Machinery Co., Ltd. Specializes in designing and manufacturing different kinds of automatic packing machines and has developed more than 80 different models, which are well applied in the food, chemical, pharmaceutical, and light industries, etc.

Based on the solid home market, Shanghai Zhonghe Packing Machinery Co., Ltd. is now gradually promoting the international market with effective and efficient sales and after sales services.

Shanghai Zhonghe Packing Machinery Co., Ltd. will continually be innovative and updating its service in all aspects to ensure that the machines are worth the trust of customers all over the world.

DCF-200 POWDER PACKING MACHINE

This series installed powder auger dosing system.can pack powder products such as milk powder, medicine and chemicals powder, etc.

Features

- Bag-making, measuring, filling, sealing, cutting and counting are all finished automatically.

2. Either under set length control or photo-electronic color tracing, we set bag length and cut in one step. Time and film saving.

3. The temperature is under independent PID control, more suitable for different packing materials.

4. The driving system is simple and reliable, and maintenance is easy.

5. Applicable material should be composite films like: PET/PE, Paper/PE, PET/AL/PE, OPP/PE.

FINISHED SAMPLE POUCH

MACHINE PICTURES

Technical Specification (FCA port Shanghai price in US$)

| Item | Description of Item | Unit Price | Qty. | Total Price |
| --- | --- | --- | --- | --- |
|  |  | in USD |  | in USD |
| 1 | Machine | Automatic Powder Packing Machine | 4650 | 1 | 4650 |
|  | Model | DCF-200 (max film width to be 180mm ) |  |  |  |
|  | Sealing type | 3-side sealing |  |  |  |
|  | Measurement | Auger type (0.5-2g，2-10g and 10-20g through replace different auger sets) |  |  |  |
|  | Hopper volume | 9L |  |  |  |
|  | Feeding way | Manual or use automatic feeder as below |  |  |  |
|  | Cutting type | Mechnical straight cutter with tear notch |  |  |  |
|  | Sealer | Horizontal andVertical sealer: diamond |  |  |  |
|  | Packing speed | 30 - 60bag/min （Depend on Products） |  |  |  |
|  | Bag size | W:30-90mm(through replace bag former) L:30-110mm(adjustable) |  |  |  |
|  | Total power | 2150W |  |  |  |
|  | Voltage | 220V or 380V |  |  |  |
|  | Weight | 190Kg |  |  |  |
|  | Machine size | L×W×H： (625x751x1558)mm |  |  |  |
|  | Material | Stainless steel 304 |  |  |  |
|  | Includes | Inverter, photo sensor, short output belt conveyor, vibrator of bag former, one bag former and one auger set |  |  |  |
|  |  | Date coding ribbon printer | 250 | 1 | 250 |
| 2 | Optional device | Shaking Auger Filler Machine Model: SLJ-100 Measurement: 0-100l Feeding heigh: 1.6m Total Power: 618W Voltage: 380V or made accordingly Machine Weight: 80kg Except motor: 304# stainless steel | 2100 | 01 | 2100 |

Guarantee: One year from the date of shipment against any manufacturing defects

Shipment: Within 10 working days from receiving 30% deposit

Payment:T/T, 30% deposit in advance and full payment before delivery

DETAILS PICTURES

1.  Powder dosing system - auger kind

It is volume way not weigh.  Press FUNTION botton, reach Fill through ▲ or ▼ to change fill amount then get different weight.

- Date coding ribbon printer

- Shaking Auger Filler Machine

Electrical Element List

| Name of Equipment | Factory Brand | Quantity |
| --- | --- | --- |
| Inverter | China ENC | 1 set |
| Decelerates motor | China Taiwan Gongji | 1 set |
| Step motor | China Jintan Sihai | 1 piece |
| Step motor driver | China Jintan Sihai | 1 piece |
| Temperature controller | China Shanghai Yatai | 2 pieces |
| Pulling film motor | China Linix | 1 piece |
| Stirring motor | China Linix | 1 piece |
| Photo sensor | China Longyi | 1set |
| Induces switch | Taiwan Roko | 4 pieces |
| Solid state relay | France Schneider | 2 pieces |
| Thermocouple | China ordered | 2 pieces |
| Pneumatic element | China Taiwan AirTAc | 1set |
| Bearings | Main from German and Japan |  |

Tool box (includes free part, free tools and doc)

- Free part with Machine

| Item | Description of Item | Qty. |
| --- | --- | --- |
| 01 | Gum over (fix the film etc) | 02 |
| 02 | Solid relay | 01 |
| 03 | Heat pipe | 04 |
| 04 | Thermocouple | 02 |
| 05 | Proximity switch | 01 |
| 06 | Fuse(set) | 01 |

- Free tooling with Machine

| Name | Spec | QTY |
| --- | --- | --- |
| socket head wrench | STD | 1set |
| cross screwdriver |  | 1Pc |
| straight screwdriver |  | 1Pc |
| screwdriver |  | 1Pc |
| scissors |  | 1Pc |
| copper brush |  | 1Pc |
| hairbrush |  | 1Pc |
| Toolbox |  | 1Pc |

- Doc with Machine

| Name | Spec | QTY |
| --- | --- | --- |
| Manual | According to ordered machine | 1 |
| Certificate of Quality |  | 1 |
| Frequency conversion manual |  | 1 |
| Temperature controller Manual |  | 1 |
| Proxmity switch Manual |  | 1 |

# Text boxes

Features

1. heating code printer

2. three lanes

3. each lane can put 13 codes (each code W2mm H3mm)

4. easy to change codes (0-9, A-Z)

5. Use ribbon, each roll 100m