SJ-55C/FM800 SJ-65C/FM1200 Rotary Head Film Blowing Machine Set

Quotation for SJ-55C:7000USD,FOB,Ningbo

Quotation for SJ-65C:11600USD,FOB,Ningbo

OPTIONAL EQUIPMENT:
1. AUTO LOADER
2. CORONA
3. DIE ROTARY DEVICE
4. AIR COMPRESSOR
5. GRAVITY METRIC DEVICE

Use and Characteristics:

It is used for blowing the various plastic film of low density polyethylene(LDPE), high density polythylene (HDPE) and linear low density polyethylene (LLDPE)

etc, Which are widely used for packing liquid, industrial products, garments and textile, Ect. And printing lamination.

The cylinders and the screw stems of the extruder are made of high quality alloy steel with optimum hardness and strong corrosion resistance after nitrogen

treatment and precision finishing. The auxiliary machine has a plat from working table for making operation easy and is equipped with bubble stab

ilizing ring.Double-rolling and double-cutting coiling unit adopts torque motor to motor to keep proper tension and make even and roll-changing easy.

| Model | SJ-55C | SJ-65C |
| --- | --- | --- |
| Screw Diameter | 55mm | 65mm |
| Screw Ratio | L/D28:1 | L/D28:1 |
| Screw Speed | 10-100r/min | 10-100r/min |
| Main Output | 50kg/h | 70kg/h |
| Power of Main Motor | 15kw | 22kw |
| Specification of Die Head | Φ100-150mm | Φ120-220mm |
| Rotational Mode of Machine Head | Continuous rotate | Continuous rotate |
| Single-sided Thickness of Film | 0.01-0.10mm | 0.01-0.10mm |
| Max. Folding Width of Film | 800mm | 1200mm |
| Total Power | 26kw | 42kw |
| Weight of Machine | 2300kg | 3800kg |
| Overall Dimensions (L×W×H) | 6000×2000× 4000mm | 6800×2400× 4800mm |

Configuration list for SJ-55C

| Extruder | Screw | Screw diameter | Φ55 |
| --- | --- | --- | --- |
|  |  | Aspect Ratio | 28:1 |
|  |  | Material | 38CrMoALA |
|  |  | Screw speed | 10-100r / min |
|  | Barrel (stainless steel heating coil heating barrel) | Barrel Cooling | air-cooled second zone |
|  |  | Cooling Motor | 350W |
|  | reducer | 180 gearbox |
|  | main motor | 15KW inverter(Huifeng) |
|  | Temperature Controller | Total 5 |
|  | Temperature Sensor | Total 5 |
| Changer | manual disassembly for network devices |
|  | changer heating | stainless steel heating coil |
| die-head | Basic Structure type | single spiral die structure |
|  | Material | 40Cr steel mold |
|  | Size | Φ80-120 mm each one |
|  | Heating | stainless steel heating coil |
| Wind Ring | Structure type | single outlet air ring |
|  | Material | Aluminum |
|  | Fan power | 1.5KW |
| foam stabilizing device | pendulum rod |
| herringbone board | wood style |
|  | adjustment | manual |
| insert edge finder | flannel style |
|  | adjustment | manual |
| Traction | Structure type | holder |
|  | traction motor | 1.5KW inverter(Huifeng) |
|  | Manual traction roller clamp clamping device |
|  | Max.Folding | 800 mm |
|  | Cots Length | 850 mm |
| winders | Single-station friction winder or Single Winder |
|  | torque speed converter | 1 |
| Traction frame | square integrated traction frame, with single-story staircase ramp |
|  | Output | 55 kg / h |

Configuration list for SJ-65C

| Extruder | Screw | Screw diameter | Φ65 |
| --- | --- | --- | --- |
|  |  | Aspect Ratio | 28:1 |
|  |  | Material | 38CrMoALA |
|  |  | Screw speed | 10-100r / min |
|  | Barrel (stainless steel heating coil heating barrel) | Barrel Cooling | air-cooled second zone |
|  |  | Cooling Motor | 0.75W |
|  | reducer: | 170 gearbox |
|  | main motor | 22KW inverter(OMRON) |
|  | Temperature Sensor | Total 6 |
| Changer | manual disassembly for network devices |
|  | changer heating | stainless steel heating coil |
| die-head | Basic Structure type | single spiral die structure |
|  | Material | 40Cr steel mold |
|  | Size | Φ160-250 mm each one |
|  | Heating | stainless steel heating coil |
| Wind Ring | Structure type | single outlet air ring |
|  | Material | Aluminum |
|  | Fan power | 1.5KW |
| foam stabilizing device | pendulum rod |
| herringbone board | wood style |
|  | adjustment | manual |
| insert edge finder | flannel style |
|  | adjustment | manual |
| Traction | Structure type | holder |
|  | traction motor | 1.5KW inverter (OMRON) |
|  | Manual traction roller clamp clamping device |
|  | Max.Folding | 1200 mm |
|  | Cots Length | 1300 mm |
| winders | Single-station friction winder |
|  | torque speed converter | 1 |
| Traction frame | square integrated traction frame, with two-story staircase ramp |
|  | Output | 30-65 kg / h |