Changzhou yanghu refrigeration equipment company.

Cold storage door series:

Half buried door :

- Product summary:

Half buried door is characterized by setting half of the door body into door frame,and it has excellent sealing and insulation performances.What’s more,it has more a beautiful appearance than normal door.

- Door panel:

The shell of door panel is assembled by plastic section bars and steel plates with polyurethane foaming inside .It has no cold bridge and is with good insulation performance .Stainless steel plates,color steel plates or embossed aluminum plate can be selected as door panels.

- Door frame

It is enclosed by high strength aluminum alloy with no process of cold bridge,and electric heating wire can be added. The whole appearance is beautiful and the door frame is serviceable.

- Accessory :

Magnetic strip is equipped with in flexible plastic which can make up slight error during manufacturing;therefore it has an excellent sealing performance.  The hinge adopts reinforced 1460hinge,which is hard and serviceable .Inside and outside handle of 1178 type door lock is connected which naturally provides safety function and enhanced safety.Electric heating film glass window is optional.

Luxury middle duty sliding door

- Product summary:

Luxury  middle duty sliding door is a new type cold store insulation panel adopting international advanced technology with nice process,excellent sealing performance,good insulation and long service life. Meanwhile,tripping safety device is equipped inside cold storage that is safe and practicable .It is suitable to cold storage door with width of less than 2.5m

- Door panel:

It is assembled by whole polyurethane foaming with panel.It has beautiful appearance and design of cold bridge,and it is with good insulation performance. Its unique round corner frame is beautiful and nice to watch. Stainless steel plates,color steel plates or embossed aluminum plate can be selected as door panels as per requirement.

- Door frame:

It is enclosed by high strength aluminum alloy with no process of cold bridge,and electric heating wire can be added. The whole appearance is beautiful and the door frame is serviceable.

- Accessory:

Guide rail is made from aluminum alloy,upper idler pulley slides stably in guide rail ,it adopts unique structure of ‘floating or opening and sinking for closing .’ idler  pulley device cooperates with tightening device to make the door separate from the door frame when it is opening and press the ground tightly when it is closing.sealing strip is made of EPDM rubber that is resistant to low temperature and high temperature.Electric heating film glass window can be optional of collision .

Return to the door :

- Product summary:

Return to the door  is characterized by leveling of the door body and door frame,it can automatically close and get tight ,it is with beautiful appearance,good sealing and insulation performance.

- Door panel

The shell of door panel is assembled by plastic section bars and steel plates with polyurethane foaming inside.It has no cold bridge and is with good insulation performance .Stainless steel plates,color steel plates or embossed aluminum plate can be selected as door panels.

- Door frame:

It is enclosed by high strength aluminum alloy with process of cold bridge,and electric heating wire can be added. The whole appearance is beautiful and the door frame is serviceable.

- Accessory:

Magnetic strip is equipped with in flexible plastic which can make up slight error during manufacturing ;therefore it has an excellent sealing performance. The hinges are hard and serviceable,open and close naturally.

Heavy duty sliding door :

1.product summary:

Heavy duty sliding door is characterized by big dimension ,it is hard and serviceable and convenient for entry and exit of vehicles.

- Door panel:

It is assembled by whole polyurethane foaming with panel,and it has beautiful appearance and design of cold bridge,and it is with good  insulation performance. Stainless steel plates,color steel plates or embossed aluminum plate can be selected as door panels as per requirements. A small door can be installed on this big door to provide convenience for the entry and exit of staff.

- Door  frame:

It is enclosed by high strength aluminum alloy with process of cold bridge,and electric  heating wire can be added.The whole appearance  is beautiful and the door frame is serviceable.

- Accessory:

Stainless steel door opener specially made as per lever principle makes opening door more convenient. Stainless ground wheel is also equipped which is serviceable. In addition ,safety tripping device is equipped to ensure safe and reliable service.Electric heating film glass window can be optional for collision.

Light duty sliding door

- Product summary :

Light duty sliding door is characterized by advantages of economic,ample,convenient,good sealing performance and reliability . It is suitable to cold storage doors with door width less than 1.5m

- Door panel:

It is assembled by whole polyurethane foaming with panel. It has beautiful appearance and design of cold bridge, and it is with good insulation performance.Stainless steel plates,color steel plates or embossed aluminum plate can be selected as door panels  as per requirements. Aluminum  plate can be selected as door panels as per requirements . A small door can be installed on this big door to provide convenience for the entry and exit of the staff.

- Door frame:

It is enclosed by high strength aluminum alloy with process of cold bridge,and electric heating wire can be added. The whole appearance is beautiful and the door frame is serviceable. Electric heating grove is preserved inside door frame.

- Accessory :

Guide rail is made from aluminum alloy,it adopts unique structure of ‘floating for opening and sinking for closing.’ to provide good sealing performance. Double bearing idler pulley with high strength is adopted to make the door slide more stable and smoothly . Tripping device is equipped to prevent people side the cold storage from trapping. Door opener adopts the lever principle to make it more convenient to open. Electric heating film glass window can be optional for collision.

Digital controlled electric sliding door

- Product summary:

Digital controlled electric sliding door adopts international advanced technology with nice process, excellent sealing performance,good insulation and long service life. Meanwhile ,door body moves stably and it has a long life service. It is suitable to cold storage door with big dimension.

- Door panel:

It is assembled by whole polyurethane foaming with panel. It has beautiful appearance and design of cold bridge,and it is with good insulation performance. Stainless steel plates ,color steel plates or embossed aluminum plate can be selected as door panels as per requirements.

- Door frame:

It is enclosed by high strength aluminum alloy with process of cold bridge,an electric heating wire can be added. The whole appearance is beautiful and the door frame is serviceable.

- Accessory

Guide rail is made from aluminum alloy,idler pulley device cooperate with tightening device to make the door separate from the door frame what it is opening and press the ground tightly when it is closing. Transmission system adopts turbo and worm for speed reducing, assisted by electromagnetic clutch to realize manual and automatic transfer,ensuring safety and practicability of the door . Its electric control system adopts original imported frequency converter to ensure its reliability. Wireless remote controller and infrared alarming system are designed to respond to different conditions to realized perfect control.wireless remote controller,anti-collision post or pulling -on-pff can be optional.

Pivoting door

- Product  summary:

It has both convenience of sliding door and sealing performance of pushing door,and it is serviceable . It has strict requirements on sealing performance,and it can be installed if there is no sliding door. This pivoting door has saved flat iron pad of traditional type and is more convenient for manufacturing and installing . What’s more ,it is more beautiful than traditional pivoting door.

- Door panel:

It is assembled by whole polyurethane foaming with panel. It has beautiful appearance and design of cold bridge,and it is with good insulation performance.its unique round corner frame is beautiful to watch. Stainless steel plates,color steel plates or embossed aluminum plate can be selected as door panels as per requirements.

- Door frame:

It is enclosed by high strength aluminum alloy with process of cold bridge,and electric heating wire can be added. The whole appearance is beautiful and the door frame is serviceable.

4. All accessories adopt stainless steel , which has greatly extended its service life and has obvious advantages compared with common hinge door and sliding door.

Double open test doors

- product summary:

Door panel is made of high pressure foaming,door adopts foaming frame with good sealing and insulation performance . Hinge and door lock exert force directly on door body, ensuring the sealing strip the able to bear temperature changing and air pressure during test. In addition,cold bridge is designed to ensure precision of the text parameters. It is preferred door for test room.

- Door  panel:

The shell of door panel is assembled by plastic section bars and steel plates with polyurethane foaming inside. It has no cold bridge and is with good insulation performance.

- it is enclosed by high strength aluminum alloy with process of cold bridge ,and electric heating wire can be added. The  whole appearance is beautiful and the door frame is serviceable .

- Accessory :

Reinforced double lock is installed in door seam,which enhanced tightening force and supporting point of the door seam. Sealing strip is made of double-hole EPDM(Ethylene-Propylene-Diene Monomer ) rubber with high resistance of low temperature and high temperature.

The above is just partly of application of polyurethane sandwich panel. If you want to know more about this wonderful products,feel free to approach us as follow :

Contact :Ellian Chen

Changzhou  yanghu refrigeration equipment co.,ltd

Address: No.63 Yang Qi Section Henglin Town,Wujin District   Changzhou city Jiangsu province.

Web:   www.yanghuvideo.com

Email: sale01@yanghuzl.com

Fax:   +86-519-88787377

Mob: 86+ 136-0159-0317

Alibaba ID : cn1511308884

QQ:   2850657693

Skype: yanghurefrigeration01