Technical Parameters of HBT30-8-60S concrete pump

| Item | Unit | HBT30-8-60S |
| --- | --- | --- |
| Theoretical concrete conveying displacement (H.P/L.P) | M3/h | 15/26 |
| Theoretical concrete output pressure (H.P/L.P) | bar | 80/50 |
| Pressure of hydraulic system | bar | 250 |
| Displacement of main oil pump | ml/r | 45 |
| Power of main power/rotation speed | kw | 60/2000 |
| Main oil pump diameter/pole diameter × stroke | mm | Φ80/φ50×1000 |
| Conveying cylinder diameter × stroke | mm | Φ140×1000 |
| Reversing times (H.P/L.P) | Time/min. | 17/29 |
| Hopper capacity × loading height | M3×mm | 0.4×1400 |
| Concrete slump | mm | 120-230 |
| Theoretical Max. vertical height | M | 150 |
| Theoretical Max. horizontal distance | M | 600 |
| Capacity of hydraulic oil tank | L | 180 |
| Capacity of water tank | L | 500L |
| L x W x H | m | 4.6x2.28x2.4 |
| Total mass | kg | 3000 |
| H.P/L.P Switch | / | Manual |
| Remote control | / | 7m wire control |

Configuration of HBT30-8-60S concrete pump

I.  Main configuration list of hydraulic system of HBT30-8-60S truck line pump（Standard）

| Name | Manufacturer | Qty. | Country |
| --- | --- | --- | --- |
| Main oil pump | LIYUAN（L10VO45） | 1 | China |
| Gear pump | WANYE（20+10） | 1 group | China |
| Mixing motor | ZHONGRUI | 1 | China |
| Main overflow valve | ATOS（20 diameter） | 1 | Italy |
| Load discharging valve | ATOS（10 diameter） | 1 | Italy |
| Electro-hydraulic directional valve | ATOS（16 diameter） | 1 | Italy |
| Solenoid directional valve | ATOS（10 diameter） | 1 | Italy |
| Air cooling | GUANHUA | 1 | China |
| Multiway valve | YOULI | 1 | China Taiwan |
| Filter | LIMING | 1 | China |
| Sealing parts | Parker | 1 set | America |
| Hydraulic hose | Manuli | 1 set | Italy |
| Adapter | EMB | 1 set | Italy |
| Pressure gauge | tecsis | 3 | Germany |
| Motor of water pump | HCHC | 1 | China |
| Water pump | HEIMAO | 1 | China |

II. Main configuration list of dynamical system of HBT30-8-60S concrete pump（Standard）

| Name | Model | Qty. | Manufacturer |
| --- | --- | --- | --- |
| Diesel engine | 4BT3.9-C80 | 1 | Cummins (China) |
| Shaft joint | FL11.5 PB-BS SAE B | 1 | Germany Raja |

III. Main configuration list of electrical system of HBT30-8-60S concrete pump（Standard）

| Name | Model | Qty. | Manufacturer |
| --- | --- | --- | --- |
| PLC(programmable logic controller) | 6ES7214-1AD21-OXBO | 1 | Germany Siemens |
| Attached module | 6ES7221-1BF22-OXAO | 1 | Germany Siemens |
| Solid-state relay | G3NA-D210B | 6 | Japan Omron |
| Fuse wire seat | PHOENIXCONTACTUK10-DREHSI | 8 | Germany Wago |
| Relay | RPF2ABD | 2 | French Schneider |
| Indicator light | 800EP-P43DLD | 5 | America AB company |
| Pumping switch | 800EP-SM323 LX20 | 1 | America AB company |
| Remote control/panel switch | 800EP-SM223 LX11 | 1 | America AB company |
| Accelerograph (jogging) switch | AR22-PR020B | 3 | Japan Fuji Co. |
| Remote control box | HY-1024BB | 1 | Germany |

只翻译一下name一栏就可以了，谢谢！