WWW.VICUTCNC.COM

Laser Welding Machine VCT-200LW

VICUT laser welding machine is perfectly used on welding Metal and alloy,stainless steel, zinc plate,iron sheet, etc.

Introduction :

1)Use imported parts such as Panasonic, Sony, etc.

2)Technology from Germany, life-time maintenance.

3)Bigger power laser is optional.

4)Can work for 24 hours without stop.

Welding Features:

1) Accurately and precision, can welding small and complex font and LOGO, quick speed, no color difference after welding, no trace, no need to handle, beautiful appearance.

2)No raised welding spot on welding surface, do not need polishing grinding process, save work time, appearance is beautiful;

3)Processing without noise, non-pollution;

4)Specific to advertising industry, special long light path, 360 degrees of arbitrary rotation, larger scale range.

5)Optional with a CCD monitor, the welding effect is more clear and intuitive.

Technical Parameters:

Laser Power                                             200W

laser wavelength                                        1064 nm

Single pulse maximum energy                               90J

The depth of laser welding                                0.1-1.2mm

The pulse width                                          0.1-20ms

Combo when the frequency of laser welding                 0.5-40Hz

Spot size adjustable range                                 0.2-2mm

The machine electricity power                              ≤9KW

power demand                                 220V　±10%/50Hz/40A

The standard workbench                         800*1000mm load200Kg

Positioning                        High-definition camera CCD synchronization

Laser travel up and down                                ≥200mm

Laser horizontal direction                              200-800mm

ANHUI WILLIAM INTERNATIONAL CNC CO.,LTD

ADD: NO.1209,XINHUA INTERNATIONAL APARTMENT,

SHUSHAN DISTRICT, HEFEI, CHINA.

WWW.VICUTCNC.COM

wmcut@vicut.cn