Coffee Roasting machine(60 kg/Batch)

Coffee bean roaster

Display

Sampler                                                    Temperature Sensor

60kg/coffee roaster

1.Description:

The machine consists of roaster and cyclone husk collector. In using, first, we should put the fresh beans in. Then , power it on. Third, the beans are roasted. Last, cool the finished roasted coffee down.

The cyclone system (dust and husk collector) will collect the dust and shell into its drawer which will help to keep the room clean.

- Features of Coffee Roaster

1. )The internal cylinder is made of thick cast iron, which helps preserve heat and controls the roasted degree, thus the coffee bean won’t be overheated and burned. The cast iron also helps save energy and reduce the gas usage.

2.) The machine is equipped with a viewing window and a sampler. The roasting degree can be observed at any time.

3. )The machine provides accurate temperature sensing, and the temperature is displayed on the screen. The baking temperature is easy to regulate.

4. )The machine is equipped with automatic ignition and flame-out protection devices. If the fire is not ignited within 22seconds, the electro magnetic valve will cut the connection between the gas and machine, thus ensure the safety of operation.

5. )With a draught fan and a big cooler pan, the coffee beans can be cooled in 1 to 3 minutes. The air from the draught fan will be discharged in other direction and has no effect on the roasted bean.

6.) Equipped with a clutch, the machine won’t be damaged when sudden power failure occurred.

7.)Our machine has collector which can collect the smoke and scraps caused during the process of roasting, thus keep the environment clean.

8.)The handle in the discharge gate is not closed to the gate so as that the heat from roasted coffee won’t harm operator.

9. )The machine has an elegant design, easy operation, compact structure and occupies little floor space

3.Technical Parameter:

| Drum Motor | 1.1kw |
| --- | --- |
| Mixer | 0.75kw |
| Cooling Fan | 1.5kw |
| Draught Fan | 0.55kw |
| Heating Mode | LPG/Natural Gas |
| Roasting Time | 15-20mins/batch |
| Capacity | Max. 60kg/batch |
| Dimension(L*W*H) | 2600x1600x2400mm(Roaster) 800x800x1300mm(Feeding Conveyor) 850x770x1850mm(Dust and Husk Collector) |

3.Price List:

| Deliver time | 25-35 days after receiving your deposit |
| --- | --- |
| Payment Terms | Full T/T |
| Port | Qingdao |
| FOB Price | USD40500 |

Trade Terms:

Payment Term: 30%T/T as advance payment,70%T/T before shipment.

Guarantee: one year after installation. If there is any breakdown caused not by misoperation reason, we would send free new parts.

Packing: standard seaworthy export packing.

-------------------------------------------------------------------------------------

Melody Tang

Tel: 0086-531-86398889

Mobile: 18764157970

Skype: melody.tang7

Email:trade@znmachinery.com

Website:http://www.foodmachinerychina.com