ZHEJIANG NEW DEBAO MACHINERY CO.,LTD

Wangsheng Road 23#, Wanquan Industrial, Pinyang, Wenzhou, Zhejiang,CHINA

Contact：Jane Chan

Skype: jane9_cn

E-mail: sale4@debaochina.com

Whatsapp/Mob: 0086-13758779899

DB-L12  Paper Cup Machine

Machine working video on YOUTUBE: http://youtu.be/_42axRWrH4U

NEW DEBAO--- Facebook Home page: www.facebook.com/dbmachine

MORE Imformation about DB-L12

Main Technical Parameter:

| Model | DB-L12 PAPER CUP MACHINE |
| --- | --- |
| Cup size | A: Top Diameter: 50~90mm B: Height:45~115mm C: Bottom Diameter: 35~64mm D: Kurling: 4.5~10mm |
| Applicable Paper | 150-250gsm (Single PE coated paper) 150~380gsm (Double PE coated paper) |
| Production speed | 45-55 pecs/min |
| Electrical requirement | Without ultrasonic：3.8KW 380V/220V 50Hz |
| Compressed air | 0.5m³/min ,Air source request (double PE): 0.4-0.6 Mpa |
| Weight | 1300 KG |
| Overall dimensions | (L*W*H ) 2600*1100*1700mm |

Warranty:We warranty 1 year from the shipment date for the machine main spare parts.The damage caused by your misuse, improper handling, neglectful maintenance, force injury and other reasons are beyond our responsibility.

Payment terms:100% T/T. 30% T/T paid as the deposit, 70%T/T should paid before the shipment.

Price: 11300.00 USD  FOB Ningbo  (This quotation validate within 30 days)

Delivery time: 30 days

Loading port: Ningbo Port

Package: Standard wooden case,1 set machine in one wooden case.

Packing Size: 2600*1100*1700mm

Gross Weight: 1300 Kgs

Main Equipment List:

| No. | Description of the equipment | Specification/Model | Quantity | Brand |
| --- | --- | --- | --- | --- |
| electric appliance | Ultrasonic | 20K | 1 PC | Shanghai-changrong |
|  | Transducer | 3G3JZ-4022 | 1SET | Japan-Omron |
|  | Contractor | LCL-D0910M7N |  | China-ZhengTai |
|  | Temperature Controller | XMTG-9031 |  | China-KeQiang |
|  | Motor | YS7134-550W | 1SET | China-QingHua |
| machine appliance | Warm gear case | WPS100-20A （1.5KW-4PB2） | 1 SET | China- Tianjia |
|  | Chain wheel | 45# steel |  | 45# 3 Rows |
|  | Chain |  |  | China- hangzhou |
|  | AXIS | 45# steal |  | 45# steal |
|  | Bearing | 6201 |  | China-haerbing |
|  | Interval gear box |  | 1 set | Shangdong |
|  | Cam |  |  | 45# |
|  | Guide Post | CR15 |  | Korea |
|  | linear bearing | LM20UU |  | China – heerbin |
|  | Cylinder | 80*125 |  | China-kaogelin |
|  | Knurling wheel | 40CR |  | CR12mov |
|  | Knurling seat | CR12MOAL |  | CR12mov |
|  | Bottom cutter | CR12MOAL | 1 set | CR12mov |