ZHEJIANG NEW DEBAO MACHINERY CO.,LTD

Wangsheng Road 23#, Wanquan Industrial, Pinyang, Wenzhou, Zhejiang,CHINA

Contact：Jane Chan

Skype: jane9_cn

E-mail: sale4@debaochina.com

Whatsapp/Mob: 0086-13758779899

DB-X16  Paper Cup Machine

Machine working video on YOUTUBE: http://youtu.be/nlTE-_D_Ro8

NEW DEBAO--- Facebook Home page: https://www.facebook.com/dbmachine

MORE Imformation about DB-X16

Main Technical Parameter:

| Model | DB-X16 PAPER CUP MACHINE |
| --- | --- |
| Cup size | A: Top Diameter: 70~100mm B: Height:60~135mm C: Bottom Diameter: 45~75mm D: Kurling: 5~12mm |
| Applicable Paper | 150~380gsm (Single PE coated paper) |
| Production speed | 50-55 pecs/min |
| Electrical requirement | 5KW 380V 50HZ |
| Compressed air | 0.3 m³/min ,Air source request (double PE): 0.5-0.8 Mpa |
| Weight | 1800 KG |
| Overall dimensions | (L*W*H ) 2800*1400*1800mm |

1 We use steel tube welding together, high strength, small deformation. All links are strengthened with double bearing structure, stable operation.

2 the part for feeding paper is same like middle speed paper cup machine feeding part,papers sucks by cam,and drop down by mechanical hands,so,it can be more steadily.

3 we use open-dividing cam running as driving system,so,it can keep higher precision and enlarge the machine life.

4 It adopts stretching punching cutter for bottom forming,and bottom looks more nice,also can reduce the bottom leak rate.

5 The Knurling parts,we adopts alloy steel, bigger push strength, higher precision, so the machine is a nice choice for customer who want high quality of paper cup.

Warranty:We warranty 1 year from the shipment date for the machine main spare parts.The damage caused by your misuse, improper handling, neglectful maintenance, force injury and other reasons are beyond our responsibility.

Payment terms:100% T/T. 30% T/T paid as the deposit, 70%T/T should paid before the shipment.

Price: 16000.00 USD  FOB Ningbo  (This quotation validate within 30 days)

Delivery time: 30 days

Loading port: Ningbo Port

Package: Standard wooden case,1 set machine in one wooden case.

Packing Size: 2800*1400*1800mm

Gross Weight: 1800 Kgs

Main Equipment List:

| No. | Description of the equipment | Specification/Model | Quantity | Brand |
| --- | --- | --- | --- | --- |
| Electric appliance | Ultrasonic | 20K | 1 PC | Shanghai-changrong |
|  | Transducer | 3G3JZ-4022 | 1SET | Japan-Omron |
|  | Contractor | LCL-D0910M7N |  | China-ZhengTai |
|  | Temperature Controller | XMTG-9031 |  | China-KeQiang |
|  | Motor | YS7134-550W | 1SET | China-QingHua |
| Machine appliance | Warm gear case | WPS100-20A （1.5KW-4PB2） | 1 SET | China- Tianjia |
|  | Chain wheel | 45# steel |  | 45# 3 Rows |
|  | Chain |  |  | China- hangzhou |
|  | AXIS | 45# steal |  | 45# steal |
|  | Bearing | 6201 |  | China-haerbing |
|  | Interval gear box |  | 1 set | Shangdong |
|  | Cam |  |  | 45# |
|  | Guide Post | CR15 |  | Korea |
|  | linear bearing | LM20UU |  | China – heerbin |
|  | Cylinder | 80*125 |  | China-kaogelin |
|  | Knurling wheel | 40CR |  | CR12mov |
|  | Knurling seat | CR12MOAL |  | CR12mov |
|  | Bottom cutter | CR12MOAL | 1 set | CR12mov |