Quotation

Description                              type                 unit price

Automatic Bag-cutting Machine            SQJ II-800              $4050

Bag-cutting Machine                      CD-II                 $530

The above price is based on FOBwenzhou port china excluding installation charge and commision.

Automatic Bag-cutting Machine

This machine can cut the woven cloth in rolls into sheet automatically as required, which is specially used for rice bags, cement bags, fertilizer bags, sugar bags, animal feed bags, etc.

It is simple and easy to operate and maintain. It reduces labor intensity, improves the production efficiency, which is an ideal equipment for bag making factory.

Main Technical Parameters:

| Model No. | SQJ II-800 |
| --- | --- |
| Max. Cutting Width (mm) | 800 |
| Cutting Length (mm) | 200-1800 |
| Weight of Cloth Roller (kg) | ≤200 |
| Power of Thermal Cutting (kw) | 3 |
| Power of Main Motor (kw) | 2.2 |
| Cutting Speed (pcs/min) | 30-60 |
| Installing Dimensions (L×W×H) (mm) | 6000×2000×1500 |
| Approx. Weight (kg) | 600 |
| Remark | Heat-cutting |

Manual Bag-cutting Machine

This machine can cut the woven cloth in rolls into sheet as required.

| Model No. | CD-II |
| --- | --- |
| Max. Width of Cloth Roller(mm) | 800 |
| Weight of Cloth Roller(kg) | ≤200 |
| Power of Thermal Cutting (kw) | 4 |
| Power of Motor(kw) | 0.37 |
| Installing Dimensions(L×W×H) (mm) | 5000×2000×1000 |
| Approx. Weight (kg) | 300 |