Cutted Cereals Bar Production Line

UU1. Flow Chart: UU

Sugar Heating Machine(Ingredients Mixer(Cereals Bar Cutting Machine with Cooling Conveyor(Packing Machine

2. Equipments List and Prices:

| No. | Commodity | Specifications | Unit Price (USD) | Quantity (set) | Amount (USD) |
| --- | --- | --- | --- | --- | --- |
| 1（optional） | Popcorn Making Machine | Great Output: about 50-60 kg per hour, Less Human Power: One worker can operate 2-3sets machine, Less Power Consumption, Safe Operation and Stable Performance | 3,000 | 1 | 3,000 |
| 2 | Sugar Heating Machine | Volume: 270L, Mixing Power: 1.5Kw, Heating Source: electricity, 18Kw, Dimension: 1300×1000×1500mm, Full stainless steel, Function: Melting and Mixing the sugar or other additives (salt, cocoa, milk, etc.). | 2,500 | 1 | 2,500 |
| 3 | Ingredients Mixer | Power: 1.5kw, Capacity: 20kg/batch, Dimension: (L*W*H) 800*900*1400mm Stainless steel Cover, Teflon food contacted parts Function: Mixing the sugar and other ingredients together. | 1,200 | 1 | 1,200 |
| 4 | Cereals Bar Cutting Machine with Cooling Conveyor | Power: 2.2kw, Dimension: (L*W*H)8500*1200*1200mm Inverters controlling the production speed, Multi-rollers flattening the mixture evenly, Blowers keeping the mixture stable. Function: Spreading the mixture onto the conveyor, cooling the spreaded mixture and cutting them into required sizes, Cooling the cutted bars and conveying them to packing | 10,000 | 1 | 10,000 |
| 5 | Packing Machine | Film Width:Max.250mm Bag Length:90-220mm Bag Width:30-110mm Product Height:Max.55mm Film Roll Diameter:Max.320mm Packing speed : 40～230bag/min Size:(L)3770×(W)670×(H)1450 Weight:550kg Fill Gas | 6,300 | 1 | 6,300 |
| Total Price | FOBQingdaoUSD23,000 |

UU

3. Specifications of Each Machine:

Sugar and Cereals Heating and Mixing Machine

It is made of Stainless steel and has heating setting to melt sugar and other ingredients, and mixer to mixing these ingredients together. It has double layer wall which keeps the temperature of mixture.

Ingredients Mixer

This machine is mainly used to mix nuts, cereals, syrup and other ingredients evenly together. Its hopper inside is made of food grade Teflon which can stand high temperature, corrosion, avoid mixture stick onto inside and hard enough for long using life. It has temperature-controller which can reserve the mixtures temperature.  It can coat sugar syrup, chocolate syrup, butter, seasoning flavors, seasoning oil on to nuts, beans, food balls etc.

Cereals Bar Cutting Machine with Cooling Conveyor

- It is mainly used to cut the mixed cereals products into required sizes and cool them down.

- It is quite simple to operate and has high capacity.

- It is controlled by two inverters which allow it finish the cross cut by one machine.

- Its strong rollers make the mixture quite flat and stick to each other tightly, avoid splitting.

- Its controller box allows operator to set the required cutting length and width freely.

- Taking very little space which allows you can use it in small work site.

- Machine parts which contact the foods are made of food grade plastic, and the machine body cover is made of stainless steel which is all suitable for food processing safety.

Packing Machine

Double frequency conversion control, bag length can be set and cut in one step, saving time and films,
Adopt PLC & HMI programming software, easy operating and setting,
Self failure diagnosis, clear failure display,

High sensitivity photocell tracing, input cutting & sealing position digitally, extra accuracy,
PID control temperature independently which is more suitable for packing different materials,
Positioned stop function, without sticking knife or wasting film,
Simple driving system, reliable working, convenient maintenance, 
All control is realized through software, easy for function adjust, technical upgrade. 
This machine is suitable for pack instant noodle, biscuit, bread, pie, snack, medicine, ice cream,

chocolate, moon cake, candy, frozen food, tissue, adhesive tape, soap, commodity, hardware parts,

cutlery, inflight meal, etc.

Trade Terms:

Payment Term: 30%T/T as advance payment,70% after shipment.

Guarantee: one year warranty. If there is any breakdown caused not by misoperation reason, we would send free new parts.

Lead Time: 30 days after receiving of advance payment.

Packing: standard seaworthy export packing.

-------------------------------------------------------------------------------------

Melody Tang

Tel: 0086-531-82316905

Mobile: 18764157970

Skype: melody.tang7

Email:trade@znmachinery.com

Website:http://www.foodmachinerychina.com