Quotation of Crusher

2015-03-27

Requirment:

- Raw material: sea salt with moisture 0.5% & 2.5%

- Feed size: 4-40mm

- Output size: 0.2-1.2mm, 0.2-0.9mm

- Capacity:20 t/h

Ⅰ- Price list

| No. | Equipment | Model | Power （KW） | Q’ty (set) | EXW Unit Price (USD) | EXW Total Price (USD) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Vertical combination crusher | PFL1000 | 45 | 1 | 6350 | 6350 |
| 2 | Belt Conveyor | B500*10m | 3 | 1 | 1670 | 1670 |
| 3 | Linear screen | 2ZS2048 | (2x2.2)*2 | 2 | 9800 | 19600 |
| 4 | Belt Conveyor | B500*10m | 3*3 | 3 | 1670 | 5010 |
| 5 | Roller crusher | 2PG610x400 | 30 | 1 | 9350 | 9350 |
| 6 | Belt Conveyor | B500*10m | 3 | 1 | 1670 | 1670 |
| Total EXW price | 43650 |
| At Current Exchange Rates: 6.0 |
| All the steel structure and bins are made in the local by client |
| The final freight will be confirmed before delivery. |

II-Technical parameters

| Name | Photo | Main technical parameters |
| --- | --- | --- |
| Vertical combination crusher |  | Model | PFL1000 |
|  |  | Feed size(mm) | 40 |
|  |  | Discharge size(mm) | 70% ＜1 |
|  |  | Capacity(t/h) | 15 |
|  |  | Motor power(kw) | 45 |
|  |  | Overall dimension(m) | 2.6*1.4*1.9 |
| Roller crusher |  | Model | 2PG610×400 |
|  |  | Feed size(mm) | 0-5 |
|  |  | Output size(mm) | ＜1 |
|  |  | Capacity(tph) | 20 |
|  |  | Motor power(kw) | 30 |
|  |  | Weight(t) | 4.0 |
|  |  | Overall dimensions(mm) | 3400×1400×1010 |
| Linear screen |  | Model | 2ZS2048 |
|  |  | Size of screen surface(m) | 2.0*4.8 |
|  |  | Number of layers | 2 |
|  |  | Motor power(kw) | 2x2.2 |
|  |  | Mesh size(mm) | 0.2-0.9-1.2 |

1.Trade terms: EXW Zhengzhou, China

2.Delivery time: Within 25 working days after recept prepayment.

3.Payment terms: 30% payment by TT ,70% before delivery by TT.

4.Guarantee: 100% brand new when leaving the factory. We guarantee quality of the machines for a period of 12 months from the trail run finish(exclude easily damageable parts). But the expense go abroad of technical engineers should be paid by buyer .

5.Installation :

If the buyer need, we will send technical engineers to the buyer’s site for technical direction, installation and commissioning. Expenses should be paid by buyer, include go abroad, round-trip tickets, hotel, food and not less than 60 dollars salary per day for each technical engineer. We are responsible to installation and equipments fluent running.

6.Services:  1),Assist clients to prepare for the first construction scheme and supply foundation drawing .

2),Install and debug the equipment

3),Training workers

4),Take initiative to eliminate the troubles rapidly

5),Provide technical exchanging

6),Provide maintenance

7.Period of validity: This quotation is avaliable in 60 days since isued.

8.Certificates:

About us: Henan Hongji Mining Machinery Co., Ltd. is a reputed manufacturer and joint-stock enterprise with import & export rights and mainly produces large and medium-sized mining machinery, metallurgy machinery and building material equipment. We are founded in August 7th, 2008 by restructuring, setting up 4 branch companies and a research center. The history of our group can trace back to Zhengzhou Huaye Industrial Machinery Co., Ltd., which was established in 1969. After more than 40 years' development, we have built into a comprehensive enterprise that comprises R&D, test, manufacture, sales and service functions.

Our headquarters, covering 80,000 square meters, is located in the Mechanical Industrial Park of Zhengzhou City, where is in the transportation junction of central China, owning more than 180 sets of heavy processing equipment with an annul output of more than 800 sets of equipment. Our fixed asset is 80,000,000 RMB (more than 11,000,000 USD).

There are more than 880 employees, including 138 middle and senior engineers and more than 200 skilled workers in our company. We have been cooperating with domestic and foreign scientific research institutes for a long time and established a testing base with domestic and foreign techniques.

Product quality and service is considered as the life of our company. All of our products have attained the certification of ISO9001:2000 qualify system. We have a group of superior experienced after-sales service members to guarantee the continuous smooth running of our products.

Maximum our customers' satisfaction is what we are keep on closing. Over the past decades, Hongji people have been innovating and transcending ourselves continuously to develop and promote the brand with quality and service. We, Hongji people, are forging ahead for first-class brand with innovative spirit and do our best to contribute to the world industry.

Key Contact: Merry Zhang (+86 158 0388 0371)

Skype:merry_hongji

Email: zoya-zhang@chinahongji.com

yifanzsj@163.com