Shandong Jinlun Machinery Manufacturing Co., Ltd

Tel: +86-15963998020                Fax: +86-6017787

E-mail: jinlun_machine@hotmail.com  Skype: jinlun_machine

Add: No58. Volvo Road, Economic Development Zone, Linyi City, Shandong Province, China.

Quotation:

| 4ft Log Debarker |
| --- |
| Length of peeler log | 1400mm |
| Max Diameter of peeler log | 500mm |
| Speed | 50 meters/min |
| Size of the blade | 1500x140x12.7mm |
| Total Power | Double roller motor 7.5 kw |
|  | Single roller motor 7.5kw |
|  | Hydraulic roller motor 4 kw |
| Overall size | 3560x2150x1100mm |
| Weight | About 2400KG |
| CIF Manzanillo | USD 6800.00/set |

| 8ft Log Debarker |
| --- |
| Length of peeler log | 2600mm |
| Diameter of peeler log | 500mm |
| Speed | 40meters/min |
| Size of the blade | 2700x180x16mm |
| Total Power | Double roller motor 11 kw |
|  | Single roller motor 11 kw |
|  | Hydraulic roller motor 4 kw |
| Overall size | 4900x2200x1450mm |
| Weight | About 4800KG |
| CIF Manzanillo | USD 11800.00/set |

| 4ft Veneer Peeling Machine (Two-in-one veneer peeling and cutting machine) |
| --- |
| Max peeling length of log | 1300mm |
| Max diameter of log | 450mm |
| Left log diameter | 28mm |
| Veneer Cutting thickness | 0.5-3.6mm |
| Size of peeler blade | 1400x180x16mm |
| Cutting speed | 48meters/min |
| Total Power | Single roller motor 5.5 kw |
|  | Double roller motor 7.5 kw |
|  | Feeding motor 5.5 kw |
|  | Slitting motor 1.5 kw |
|  | Conveyor motor 1.5 kw |
| Total weight | About 3800KG |
| Overall size | 2800x2100x1350mm |
| CIF Manzanillo | USD 14500.00/set |

| 8ft Veneer Peeling Machine (Two-in-one veneer peeling and cutting machine) |
| --- |
| Max peeling length of log | 2600mm |
| Max diameter of log | 450mm |
| Left log diameter | 35mm |
| Veneer Cutting thickness | 0.5-3.6mm |
| Size of peeler blade | 2700x180x16mm |
| Cutting speed | 48meters/min |
| Total Power | Single roller motor 7.5 kw |
|  | Double roller motor 5.5 kw*2 |
|  | Feeding motor 5.5 kw |
|  | Slitting motor 3 kw |
|  | Conveyor motor 4.5 kw |
| Total weight | About 7800KG |
| Overall size | 5000x2450x1450mm |
| CIF Manzanillo | USD 25800.00/set |

Notice:

1. MOQ: 1 set

2. Payment term: T/T 30% as deposit and 70% balance paid before loading

3. Lead time: 25 days after received the deposit

4. Packing: Nude

5. Valid time: 15 days start when it was sent

Best regard

jimmy

Shandong Jinlun Machinery Manufacturing Co., Ltd

Tel: 86-15963998020

Fax: 86-539-6017787

Skype: jinlun_machine

E-mail:jinlun_machine@hotmail.com

Web: www.timber-machinery.com

Add: No 58. Volvo Road, Economic Development Zone, Linyi City, Shandong Province, China.