Quotation of dryer for Cow dung

2015-04-15

Requirements:

- Raw material: Cow dung

- Input mositure of raw material: 90%

- Output mositure: 40-60%

- Capacity: 0.5 m³/h

- Heat: gas

| Name | Picture | Technical parameters | Unit Price (USD) |
| --- | --- | --- | --- |
| Concentrated tank | Will be maked onsite by user |
| Rotary Dryer |  | Type | Ф600x6000 | USD 10800 |
|  |  | Diameter | 0.6 |  |
|  |  | Длина барабанна(м) | 6 |  |
|  |  | Gradient(%) | 3-5 |  |
|  |  | Rotational speed(r/min) | 3-8 |  |
|  |  | Power(kw) | 3 |  |
|  |  | Inlet air temperature(℃) | ≤700 |  |
|  |  | Weight(t) | 2 |  |
| Including: body, feed end and output end, motor, reducer, gearing, wheel gear, rolling ring, carrier roller group and Gas burner. |
| Cyclone dust collector |  | Including: 1 cyclone with diameter 0.5 m, motor power of fan is 3 kw, connected pipe with dryer and fan. |
| Output Belt Conveyor |  | B500x10m | 1 set | USD 1670 |
| Dehydrator |  | Model | HJ-10 | USD 3000 |
| EXW Total USD 15470 |

Attention!  The final freight will be confirmed before delivery.

1.Trade terms: EXW Zhengzhou, China

2.Delivery time: Within 25 working days after recept prepayment.

3.Payment terms: 30% payment by TT ,70% before delivery by TT.

4.Guarantee: 100% brand new when leaving the factory. We guarantee quality of the machines for a period of 12 months from the trail run finish(exclude easily damageable parts). But the expense go abroad of technical engineers should be paid by buyer .

5.Installation :

If the buyer need, we will send technical engineers to the buyer’s site for technical direction, installation and commissioning. Expenses should be paid by buyer, include go abroad, round-trip tickets, hotel, food and not less than 60 dollars salary per day for each technical engineer. We are responsible to installation and equipments fluent running.

6.Services:  1),Assist clients to prepare for the first construction scheme and supply foundation drawing .

2),Install and debug the equipment

3),Training workers

4),Take initiative to eliminate the troubles rapidly

5),Provide technical exchanging

6),Provide maintenance

7.Period of validity: This quotation is avaliable in 60 days since isued.

8.Certificates:

Key Contact: Merry Zhang (+86 158 0388 0371)

Skype:merry_hongji

Email: zoya-zhang@chinahongji.com

yifanzsj@163.com