QX-Rd round cotton pad machine

- Adopt consistent operation way, from raw materials by the automatic transmission, heating embossing, punching cutting piece, arrangement discharge, waste the winding, automatic counting.

- The machine adopts mechanical pressure material, four groups of circular knife molding composition, and with the most reasonable dislocation arrangement (the domestic leader), make the raw material loss dropped to the lowest, product cost reduction, product efficiency relative to improve. The mould is made of imported high-speed steel. It adopts Japanese walk silk processing.  Error is less then 0.01mm. Long service life.

- The machine adopts international high-quality steel, with steel to steel embossing rollers (embossing or not).Circular punching mould is made of imported high-speed steel. Through walk silk cutting processing. Cutting accuracy, without burr, high precision. It equips 3 feeding rollers and you can feed one roll of cotton or two rolls of spun-lace nonwoven and one roll of cotton for recombination. When you just use one roll of cotton, the other two feeding rollers can be used for prepare material. It adopts servo motor for counting and output as half piece of round cotton pad. The machine suitable for different kinds of material. The rack of machine is made of strong material; the brand of bearing is NSK.

- The machine has five tension control device and waste automatic rolling device. It equips four high precision oxidation aluminum rollers for spread the material.

- The machine adopts automatic counting device. The width of raw material according to the size of mould. The max diameter of raw material is 70cm.

- The machine adopt adopts CAM transmission with two sets of special wear-resisting rubber roller conveyor, others are 5 high-precision oxidation aluminum alloy with fabric guide roller for conveying. It equips heat embossing device.

- The machine adopts Siemens frequency converter 5.5kw Siemens motor, wiring standard that a reasonable, safe and convenient operation.

- The machine can produce discharge makeup cotton edge open or not. (has been successfully developed edge belt hole type wafer discharge makeup cotton)

| Type | QX-Rd |
| --- | --- |
| Producing speed | About 400pcs/min |
| Nominal voltage | 380V |
| Rated frequency | 50Hz |
| Total power | 7.5kw |
| Dimension | L:5000mm*W:1000mm*H:2000mm |
| Weight | 2900kg |

The price of QX-Rd round cotton pad machine is USD22150. （FOB Shanghai）

Main parts:  Siemens frequency converter, Siemens motor, Schneider touch screen, Schneider servo motor, other electric equipments and switches are imported form Japan Mitsubishi.

The main machine: It equips three feeding rollers and you can feed one roll of cotton or two rolls of spun-lace nonwoven and one roll of cotton for recombination. When you just use one roll of cotton, the other two feeding rolls can be used for prepare material. The embossing rollers are solid for a long time working. The punching mould is made of imported high-speed steel. The mould is easy to change; you just need loosen four screws.

Counting system: It adopts serve to control the punching position. It will punching a little at the cotton pad when it reach the number of you set on the touch screen. The punching position can be adjusted in order to lesser waste.

You can see clearly of counting in the following picture.

Our company has technology patents of cotton pad machine.

Jiaxing Ruixing Machinery Co., Ltd.

Tel: 008618257317361

Add: No.120 Fengyuan Road, Nanhu Industrial Garden, Jiaxing City, Zhejiang Province, China

2015-4-23