Quotation

Description                              type                 unit price

Recycling Granulator                  YF-FL150-II                $8800

The above price is based on FOBwenzhou port china excluding installation charge and commision.

Recycling Granulator

It's used for processing old woven bag, plastic film or other broken old plastic to make them into granules that will be reused as raw materials.

| Model No. | SJ-FL150-II |
| --- | --- |
| Diameter of Screw (mm) | 150 |
| L/D Ratio of Screw | Main Screw:10:1 |
| Rotational of Speed Screw (r/min) | 50-80 |
| Power of Motor (kw) | 37 |
| Power of Sub-motor (kw) | 11 |
| Motor Power of Grain Cutting (kw) | 3 |
| Heating Power (kw) | 30 |
| Production Capacity (kg/h) | 80-120 |
| Overall Dimensions (L×W×H) (mm) | 5000×2000×1300 |
| Approx. Weight (kg) | 1400 |