1100&988 Roll Forming Machine

| No. | Item Name | Lead Time | Package | Qty | Price/USD FOB TIANJIN |
| --- | --- | --- | --- | --- | --- |
| 1 | 1100&988 Roll Forming Machine | 40 days | 40′ | 1 | 16000 |

1. Panel drawing and machine picture(picture is just for reference)

- Technique parameters

(1) Processing material: aluzinc/galvanized steel/colored steel coil

板材：镀锌卷，彩涂卷

- Material thickness: 0.3-0.8mm

板厚

- Effective width: 1100/988mm

有效宽度

- Feeding width: 1250mm

展开宽度

- Main motor power: 4 kw

电机功率

- Pump power: 4 kw

泵站功率

- Shaft diameter: 75mm

轴径

(8) Forming steps: 13/13 steps

成型排数

(9) Roller material: 45# forged steel, with hard chrome plating

轴材质：15#镀铬

(10) Main frame: 350H steel

大架

(11) Medium plate thickness: 16mm

中板厚度

(12) Control systerm: PLC computer control with inverter

控制系统：PLC带变频器

(13) Power supply: 380V, 3 Phase, 50Hz

电压

(14) 0veral sized: 6500mm*1500mm*1500mm

尺寸

(15) Weight: about 4 tons

重量

3. Work flow

Manual decoiler—Roll forming machine—PLC control—Hydraulic system —Post cut—Output table

上料架--成型机--PLC控制箱--液压系统--剪切--接料架

- Components of production line

| No. | Name | Unit | Qty |
| --- | --- | --- | --- |
| 1 | Manual decoiler | set | 1 |
| 2 | Main forming machine | set | 1 |
| 3 | PLC control system | set | 1 |
| 4 | Hydraulic pump station | set | 1 |
| 5 | Post cut | set | 1 |
| 6 | Electric motor | set | 1 |
| 7 | Output table | set | 1 |

5. Payment term

TT, you should pay 30% as the deposit on the order day, then pay 70% before delivery when you inspect goods well in factory or by video

- Warranty

12 months, and lifelong technical support service