Paste Grinder LTMJ-1

The machines are beautified. The bottom frame and motor are covered by stainless steel.

Product It could make:

- Introduction:

The paste grinder is the processing machine for colloidal products. It has functions of cracking, cutting, milling, mixing, etc. After processing, the granularity can be 2-50um, the homogeneity is above 90%. It is the ideal processing machine for paste products production. The machine can be used in line of businesses of food, medicine, chemical, etc.

- Technical Parameter:

| Model | LTMJ-1 |
| --- | --- |
| Capacity | 10-20Kg/hr |
| Finess | 2-50um |
| Inlet Size | Ø90mm |
| Dimension | 530x260x580mm |
| Weight | 60Kg |
| Power | Single-phase OR 3-phase,4Kw |
| Grinding Speed | 3000RPM ± 100RPM |
| FOB Qingdao Price | USD 1200.00 |

We also have the whole production line:

TERMS

Payment Term: 100% T/T payable

Lead Time: 7 days after receiving of advance payment.

Packing: standard seaworthy export packing.

Required Containers: consolidated container

Melody Tang

Tel:0086-531-82316905

18764157970

Skype: melody.tang7

Email:trade@znmachinery.com

Website:http://www.foodmachinerychina.com