Shandong Jinlun Machinery Manufacturing Co., Ltd

Tel: +86-15963998020                Fax: +86-6017787

E-mail: jinlun_machine@hotmail.com  Skype: jinlun_machine

Add: No58. Volvo Road, Economic Development Zone, Linyi City, Shandong Province, China.

Quotation:

Simple 8ft veneer peeling line

| Type | Picture | Unit price | Quantity | Total |
| --- | --- | --- | --- | --- |
| Log debarker |  | $12000 | 1 | $12000 |
| Veneer peeling machine |  | $26000 | 1 | $26000 |
| Log loader |  | $2500 | 2 | $5000 |
| Total price FOB QINGDAO | $43000 |

| 8ft Log Debarker |
| --- |
| Length of peeler log | 2600mm |
| Diameter of peeler log | 500mm |
| Speed | 50meters/min |
| Size of the blade | 2700x180x16mm |
| Total Power | Double roller motor 11 kw |
|  | Single roller motor 11 kw |
|  | Hydraulic roller motor 4 kw |
| Overall size | 4900x2200x1450mm |
| Weight | About 3800KG |
| FOB Qingdao | USD 12000.00/set |

| 8ft Veneer Peeling Machine (Two-in-one veneer peeling and cutting machine) |
| --- |
| Max peeling length of log | 2600mm |
| Max diameter of log | 400mm |
| Left log diameter | 35mm |
| Veneer Cutting thickness | 1.0-3.0mm |
| Size of peeler blade | 2700x180x16mm |
| Cutting speed | 35meters/min |
| Total Power | Single roller motor 7.5 kw |
|  | Double roller motor 5.5 kw*2 |
|  | Feeding motor 5.5 kw |
|  | Slitting motor 3 kw |
|  | Conveyor motor 4.5 kw |
| Total weight | About 7800KG |
| Overall size | 5200x2350x1450mm |
| FOB Qingdao | USD 26000.00/set |

| Log Charger |
| --- |
| Type | 2600 |
| Power | 3KW |
| FOB Qingdao | $2500/set |

Notice:

1. MOQ: 1 set

2. Payment term: T/T 30% as deposit and 70% balance paid before loading

3. Lead time: 25 days after received the deposit

4. Packing: Standard export loading

5. Valid time: 15 days start when it was sent

Best regard

jimmy

Shandong Jinlun Machinery Manufacturing Co., Ltd

Tel: 86-15963998020

Fax: 86-539-6017787

Skype: jinlun_machine

E-mail:jinlun_machine@hotmail.com

Web: www.timber-machinery.com

Add: No 58. Volvo Road, Economic Development Zone, Linyi City, Shandong Province, China.