温州市益彰贸易有限公司

#### WENZHOU CHANGS INTERNATIONAL

ADD:#1105,Guoguang Mansion     发    票             No : 0615CHS15

(Opposite railway station

PROFORMA   INVOICE       DATE:15th JUNE /2015

# WENZHOU CHINA

Tel:+86-577-86051848

ATTN: Didier Vandenbon  Dakar Sénégal

| Number | Description &Specification | Quantity | Unit Price | Amount |
| --- | --- | --- | --- | --- |
|  | MULTILAYER KRAFT PAPER BAG MAKING MACHINE FL-1200 Four Color Flexo Press Inland charge from factory to Shanghai port This machine line need One 20GP container and one 40 HQ container Total 1, Delivery time: within 45 workdays to finish the machine production after reciving 30% payment by T/T 2, Country of Origin: China 3, Payment Term: 30% as deposit, 70% balance after inspection before shippment 4,Warranty: 1 year limited warranty after installation. 5, Installation and Training: we can send 2 engineers to buyer factory to install and set up the machines, but all the charges for our engineers should be paid by buyer, including round trip tickets, visa, accommodation cost, traffic cost, 120USD of salary per person every day, etc. Bank Information BENEFICIARY：WENZHOU CHANGS INTERNATIONAL ADD:#1105,GUOGUANG MANSION,(OPPOSITE THE RAILWAY STATION),WENZHOU CHINA BANK :BANK OF CHINA WENZHOU BRANCH MAIN BUILDING OF XIHU JIN YUAN WENZHOU CHINA SWIFT:BKCHCNBJ92B A/C NO.:3506 5834 2969 | 1Set 1SET | FOB USD52700.00 USD32000.00 | SHANGHAI port USD52700.00 USD32000.00 USD1500.00 USD84700.00 |

MULTILAYER KRAFT PAPER BAG MAKING MACHINE

Video: http://v.youku.com/v_show/id_XMTU3NDkwNTQw.html

It is a multilayer kraft paper bag making machine,it is a green product without pollution.

It is suitable for making bag with kraft paper of 70-80 gsm with roll paper.

It can complete the steps of automatic feeding,side gluing,tube-forming,cutting and delivery.

Main Technical Parameter:

| Bag length: 400-1500 (also can be customize) | Bag width : 350-650mm |
| --- | --- |
| Paper weight : 70-140 gram | Material width: 620-1250mm |
| Speed: 40-60pcs/min | power：11.2KW |
| Kraft paper layers : 2-3layer | Machine weight : 4000kg |

FL-1200 Four Color Flexo Press

Max Paper Width: 1200mm

Video link: http://v.youku.com/v_show/id_XMjgxNDYyOTQ0.html

Features:

1, shape innovative, institutional rational, advanced technology, simple operation, stable overprint, print quality, print speed, very low reject rate, long service life, easy maintenance
2, using Taiwan's main line of motors and motor Mexico, Japan, frequency control, saving electricity, running small fluctuation
3, down version of automatic cut-off line ink motor, automatic start-line version of ink from device
4, using the Japanese SNK imported bearings (one-way bearings used in Germany)
5, starting with the fall edition version of the system or using YUKEN SMC pneumatic system
6, at the end of a special steel roller using the German process, and after special treatment, and plating 10 wire-thick protective layer of hard chromium, beating the 0.01mm below

7, with separate oven and the cold wind bellows shape, can effectively prevent the adhesion of printing ink after
8, Unwinding from Taiwan automatic gas control system of hydraulic correcting knitting machine
9 Unwinding and Winding with Japan's Mitsubishi powder, Taiwan automatic constant tension control system