JL45 Normal Zipper Extruder

Usage:

- This extruder is used to make LDPE and PP material zipper Profile.

- This extruder can produce various types of zipper (strip) through changing its die plates

- The die plates can be designed according to customer's sample(requirement)

- This extruder consists of chiller, main extruder, die head, die plates, water tank (form the zipper at constant temperature), dewater device and air-drying device, traction part, zipper closing part and zipper winding part.

- This extruder can produce high quality zipper profile in high speed and stable process, its quality, output and service got great repute from our customer all over the world.

Characteristic:

- According to the special demand of the material flow rate during the process of making zippers the charging barrel and the screw that the machine employs are made of the high quality alloy steel, and they are chrome plated, having the features of strong abrasive resistance, heat resistance and deformation resistance.

- The heating band of charging barrel adopts the stainless steel out cover, with independent air blower for cooling, inside it adopts porcelain heating circle.

- The filter net of the die head adopts the integral type one, which is easy to unpick and wash.

- This machine employs the stainless steel storage tank.

- The main vice motor of this machine adopt Panasonic frequency converters，and domestic famous brand hard tooth-faced speed reducer and the torque motor reeling machine, which all make it stable to make zippers, the quality and the output of the zipper can be improved.

- The power supply connection adapts the air plug.

- The winding part adopts frequency controller to improve the quality and output of zippers.

- The live-rollers of the front and back traction part adopt two Turbine decelerating motors to grouping frequency control of the motor speed. (Before the live-rollers are connected by belt, and adopt one set of cycloidal pinwheel reduction motor.

- The plane of worktable adopts the stainless steel plate.

- The electrical appliances of this machine all use the Schneider brand Electric, and the temperature controller used Omron. The appearance of this machine is very attractive and easy operation.

11. The material hopper of this machine uses the automatic suctions, which made in Hong Kong.

Choice

Choice 1: JL45 Normal Zipper Extruder, to produce normal LDPE, PP Zipper.

Choice 2: JL45 Normal Zipper Extruder with one set of JL20 Extruder for color line, to produce zipper with one color line.

Choice 3: Modified JL45 Zipper Extruder with two sets of JL30 Extruder for color strip, to produce double color zipper.

Choice 4: Modified JL45 PVC Zipper Extruder, to produce PVC Zipper.

MACHINE TECHNICAL PARAMETER:

| Model | JL-45 |
| --- | --- |
| Material | LDPE,PP |
| Speed | 10-50meter/minute |
| Zipper width | 3-50 mm |
| Thickness of zipper | 0.3-2.2mm |
| Diameter of screw | 45mm |
| Draw ratio of screw | 30:1 |
| Main motor | 5.5kw |
| Power of the auxiliary motor | 1.1 kw |
| Power of cooling water machine | 1.5kw |
| Power of Dehydration and drying | 2kw |
| Winding machine | 1.1kw |
| heater | 6.8 kw |
| Power | 22 kw |
| Overall dimensions | 9350X1300X2200mm |

Wenzhou Xinda Zip Lock Bag Making Equipment CO.,LTD

555 the second road ruian economic development zone,wenzhou city,zhejiang province,China.

Tel:86-577-65155000     Fax:86-577-65155080  Mob:86-15888200169   nora1176@xindamachine.com

Skype: norashao1

ADD：555 the second road ruian economic development zone, Wenzhou city, Zhejiang province, China

TEL：86-577-65155000　65155077   FAX：86-577-65155080  nora1176@xindamachine.com