Quanzhou Huaxun Machinery Making Co., LTD

Address: NO.3,Qipei Street, Gudian Community jinlong Sub-district, Licheng District, Quanzhou City, Fujian Province, China   Post code:362000

Tel ：+86-0595-22422828     Fax：+86-0595-22422727

Email:christine@papermachine.cc Skype:christine08281

TradeManager:cn1001130452  QQ:1811989902

Website：http://www.papermachine.cc  http://huaxun.en.alibaba.com/

Price Expiry Date: August 30th, 2015.

| PICTURES OF EQUIPMENT | MAIN TECHNICAL PARAMETER | UNIT PRICE(FOB price) |
| --- | --- | --- |
| HX-170/400（300）Folding Napkin Paper Machine(with two colors printing) | 1.Design Production speed: 400-600 pieces/minute 2.Folded size:150*150mm 3.Unfolded size: 300*300mm 4. Raw paper diameter: ≤1200 mm; raw paper width: 300mm. 5. Equipment power: about 4.5Kw (380V 50HZ) (excluding power of both heating device and drying device). 6. About 1.65 tons 7.Equipment over size (L×W×L): about 3700 * 730 *1600 mm 8.It can produce 2 plies' napkin paper which should be 13-18g/m2, 1 ply's napkin paper which should be 22-40g/m2. | USD 10.500 （with one embossing unit ,with two colors printing） |
| Model HX-002 Polybag Bagging and Sealing Packaging Machine (Semi-Automatic) | (1).Packing speed: 8-10 bags/minute; (2).Power supply voltage: 220V, 50HZ; (3).Air supply voltage: 0.5MPA (client should prepare this by himself); (4).Total power: 0.4KW; (5).Packing size (L×W×H): the sizes should be decided by the buyer,width is fixed, height should be more than 50mm, can be +-50mm. (6).Machine size: 1380×800×1020mm. (7). Machine Weight: 0.3ton. | USD 2,800 for packing napkin paper. |

REMARKS:

1、FOB price;

2、Warranty of the equipment：One year. The spare parts will be replaced freely by the seller within one year (exclude wearing parts). The express cost of parts should be paid by the buyer. After one year, the seller will carry on the tracking of technology and quality. The seller will provide the buyer with wearing parts which has good quality and preferential price in a long time.

3、Package：Wood Pallet and plastic film.

4、Terms of payment：it will be 30% down payment by T/T before production, then balance by T/T before the machines leave out of the seller’s company. After the seller receives all related balance, then the seller will begin to send goods to the port. The production of machine will need about 120 working days.

5. Installation and training: the seller will send technician to the buyer’s factory to install and adjust the machine if the buyer ask for this. All the expenses of the technician including two-way air tickets, accommodation(food and room), transport (bus fee, etc), and salary(salary is USD85 / day for each technician) is to be paid by the buyer. The buyer should make ready for workshop, power, raw materials in advance, then the period for the installation and adjustment and training will be totally within about 20 working days.

Some photos about packaging