MACHINE PICTURES

Technical Specification and Price

1.Multi head weigher (10 heads)

Feature:

1. Instantaneous reaching of correct calculating by high-precision load cell.

2. Quiet running, stable action and long life by adopting step motor.

3. The open & close speed of the material bucket cover can be finely regulated according to the features of the measured material to prevent crashing and damage.

4. Neatness and hygiene by using stainless steel as the material of its parts.

5. Excellent compatibility and easy using with other packing equipment

Application

the pellets, bar, brain shape material. Such as puffed food, candy, small biscuit, vegetable slice, nut, fried material, pet food, small hardware etc.

Technical Specification

| Name | 10 head weigher |
| --- | --- |
| Brand | High dream |
| Max Weight | 1000g/time |
| Weighing Range | 10-1000g |
| Weighing Accuracy | ±0.3-1.5g |
| Hopper Capacity | Max 3000cc |
| Weighing Speed | Max 60 times/min |
| Total power | 220V 50Hz 1.5Kw |
| Control | 7” panel |
| Material | Stainless steel 304 |
| FOB port Shanghai in USD | 10,000 |

- Shaking feeder + Z type elevator + platform

Feature:

- The support platform works with combined weighing packaging machine to support the multihead weigher.Powder coated carbon steel or stainless steel material.

2.1 The elevator and electronic metering scale shall be used together, control circuit is used to control the position of the material, realizing automatic feeding and stopping function.

2.2  The elevator can be made of stainless steel and carbon steel according to the customer choice.

Application

- Put weigher on the support platform

- Z type elevator suitable for the lifting of frangible and non-frangible material such as potato slice, prawn cracker, crispy rice, metals and medicines etc.

Technical Specification

| Power | 220V,50/60Hz,40W |
| --- | --- |
| Conveying Speed | 60 bags/min |
| Material | Stainless steel 304 |
| FOB port Shanghai in USD (whole set) | 8.350 |

# Text boxes

Z type elevator

Shaking feeder

Platform

Without Check weigher

Multi head weigher 10 heads

Guarantee: One year from the date of shipment against any manufacturing defects

Shipment: Within 30 working days from receiving 30% deposit

Payment:T/T, 30% deposit in advance and full payment before delivery

Guarantee: One year from the date of shipment against any manufacturing defects

Shipment: Within 20 working days from receiving 30% deposit

Payment:T/T, 30% deposit in advance and full payment before delivery

Space of platform

L1800*W1800-H1700mm

Without Packing machine

Whole system include feeding and weighing system: USD10,000+USD8,350 = USD18,350

Without Output conveyor