FORMAL QUOTATION

To:                                       Invoice No.: FYVV15071001

#### Date: July 10th, 2015

Seller:	ZHEJIANG FEIYUN TECHNOLOGY CO., LTD

ADD: NO.281 YANJIANG WEST ROAD, RUIAN, ZHEJIANG, 325200 CHINA

Tel: 86-577-65676922 	 Fax: 86-577-65068766

Mobile: 86-13958850611

Represented by: Vivian

We hereby confirm having sold to you the following goods on the terms and conditions stipulated below:

| DESCRIPTION AND SPECIFICATION | QTY | UNIT PRICE FOB (USD) | AMOUT FOB (USD) |
| --- | --- | --- | --- |
| NJP1200 Capsule filling machine (including one set of mold, dust collector, PLC and touching screen, water vacuum pump) | 1set | 28000.00 | 28000.00 |
| Vacuum Charging machine | 1set | 3000.00 | 3000.00 |
| Capsule Sorting Polisher JFP-110 | 1set | 3000 | 3000.00 |
| Metal Detector for Medicine | 1 set | 10800.00 | 10800.00 |
| Total:USD |

Other terms and conditions:

- Price terms: FOB Shanghai or Ningbo

- Delivery date: 58 working days after mould confirmed and advanced payment received.

- Loading port: Shanghai or Ningbo port

- Installation and commissioning: The seller will send the technician to user’s site for 7 days-10 days, the round international air ticket and accommodation in abroad would be arranged by buyer’s. The buyer should pay our technician $50 each day

- Payment: 30% deposit in advance, 70% payment before sending the machine.

- Validity of price: 2 month

And the above price I offered for one order to ship together.

Look forward to receiving your early confirmation.

Best regards with thanks,
Vivian  / Oversea Sales

E-mail: sales4@feiyun.com  mobile: 0086-13958850611

NJP-1200C FULL-AUTOMATIC CAPSULE FILLING MACHINE

- Introduction

The machine is a precise intermittence motion capsule filling machine. It is suitable to fill powder, grain and pellet into 0#--5# hard capsules, particularly useful in mass production. The machine can automatically complete the process of feeding capsule, detaching capsule, filling, rejecting defective capsule, closing capsule, discharging finished capsule. It has advantages of accurate orientation, freely adjusting dosage, high finished rate, small in shape, and easy in operation. Its performance has passed the provincial technical appraisal and could completely fulfill the “GMP” requirement.

- Performance and features:

1). The max output is 72000 capsules /hour

2). SIMENS PLC control and SIMENS tracking system

3). Cantilever type touch screen
4). Detector for lacking of material and capsule

5). Fitted with the latest close type rotary table and filling dosage device

6). Easy to operate, clean and exchange mould

7). High-precise graduator and generation device

8). All cam is nitrided, increasing surface hardness

9). Wholly meet the GMP requirements and CE certificate

10). It has passed the provincial technical appraisal

11). On the basis of model NJP-1200B, model NJP-1200C is equipped with touching screen, PLC, intelligent module, fiber sensor and imported components: motor reducer, vacuum pump, graduator, and feeding motor. So it has advantages of easy operation, high automation, and stable running.

- The technical specifications:

| Productivity | 1200 Pcs/min |
| --- | --- |
| Size of Capsule | 00#-5# |
| Filling Percentage | ≥ 99.8% |
| Dosing Precision | < 4% |
| Power supply | 380V 50Hz 3-phase 4-wire |
| Power | Total 5.8 KW |
| Water supply | Supplied with circulation water box. Exterior water Supply can also be connected. Water flow: 500L/h, 0.1-0.2 MPa |
| Dust collector | Capacity 210m3/h |
| Overall dimensions | 970X800X1870(+250) mm |
| Weight | 1200Kg |
| Working Condition | Environmental Temperature: 20-25 ℃ Relative humidity:40-50% Powder Granularity :40-80 mesh Pellet Granularity:10-15 mesh |

# List of Key Parts of NJP-1200C

（PLC and computer controlled soft made by Siemens Co.）

| Name | Model | Manufacturer |
| --- | --- | --- |
| Touch Screen | Smart 300 | Siemens, Germany |
| Programmable controller | 6ES7214-1BD21-0XB0 | Siemens, Germany |
| Intelligent module |  | Siemens, Germany |
| Inverter | MMV150/3 | Siemens, Germany |
| Power supply | 6EP1331-1SH01 | Siemens, Germany |
| Linear bearing |  | Korea, Japan |
| Rolling wheel bearing |  | Korea, Japan |
| Linear oil less bearing |  | Germany |
| Water Ring Vacuum Pump | 060 | The joint venture company |
| Main motor | 1HPX4P, 0.75KW | Taiwan |
| Intermittent generation graduator | RU-83DS-06-120-2R-V RU-83DS-12-120-2R-V | Taiwan |
| Model K-TP178 PLC (man-machine interface)， <The soft made by Siemens> | Siemens, Germany |