# Specification：

| ITEM | DESCRIPTION |
| --- | --- |
| Portable Industrial Design | Portable compact host, Select different cameras based on occasions, portable charging by docking station |
| GUI | Setup system parameters through the Panel controller |
| Language | Chinese, English, other(optional) |
| Security | User password management |
| Video and preview | Video input | Video Compression Criteria |
|  | OSD | Overlays letters… like date & time information and vehicle ID into video streaming |
|  | Video Compression Criteria | H.264.With Hisilicon technology |
|  | Dual stream | Support |
|  | Resolution | Support CIF、HD1、D1 |
|  | Video quality | 1-4 levels, 1 is the highest level and 4 is the lowest level |
|  | Video Bit Rate | CIF: 400Kbps ~ 1.5Mbps |
|  |  | D1: 1000kbps ~ 2Mbps |
|  | Preview | Real time, record video preview |
| Audio | Audio Input | MIC input |
|  | Audio Output | Headphone output |
|  | Compression | G.726 |
| Record | Storage | Micro-SD card: support 1G~64G |
|  | File Type | H.264 ASF、FAT32 |
|  | Recording Mode | Default auto recording after power on, support manual recording |
|  | Video Search | Search video by time , type |
|  | Video playback | Support forward and backward at the speed of: x2, x4, x8, x16, support playback of file by time |
| LCD parameters | Size | 2.4 |
|  | Type | TFT |
|  | Resolution | 480*234 |
| Wireless transmission | Built-in 3G wireless transmission module, WCDMA, CDMA2000, TD-SCDMA system optional; |
|  | Compatible with GPRS, EDGE; |
|  | Support up to 4G;(optional) |
|  | Built-in WIFI |
| GPS | Built-in GPS or BeiDou; |
| Upgrade | Upgrade by SD card or USB |
| External Interface | Support data export to USB, Interface charge |
| Power &consumption | Power management | Manual startup/shutdown; support manual off-screen, automatic off- screen |
|  | Battery capacity | 2400mAh , 7.4V |
|  | Charging period | < 3 hours |
|  | Working period | >= 5 hours |
| Working environment | Operating temperature | -20℃ ~ +50℃ |
|  | Operating Humidity | 10% to 95% |
| Dimensions | 80(W) x140(H) x33(D) mm |

# The Diagram Of Attachments：

# Text boxes

- HD screen

2.4” TFT, resolution:480*240, Image is exquisite, colour is real, provides prefect display effect

- Flexible way of wearing

Wear comfortable casual. For handheld, his hips and shoulders wear to wear a variety of ways, Overall the characteristics of both the practical and concise design.

- Features

◎ IP65 Industrial level material, Ip65

◎ power on quickly

◎ Main device and camera separation design;

◎ Lithium battery power supply

◎ GPS ,3G/4G and WIFI function;

◎ Working time >=5 hours;

◎ A variety of network function, including real-time preview, remote playback, remote download, radio, intercom, message;

◎ Support different transport quality.

◎ 64G One micro-SD card, support 64G;

◎ IP intercom (optional)

◎ Support mobile control management platform (optional)

Portable Digital Video Recorder  M503

Applications：

- Traffic police

- Patrol

- Patrol

- Coastal defense

- Armed police

- Insurance

- Railway

- The courts

- Energy

- Enterprise search

- Interview object