Quotation  Sheet

Quotation No.: SN20150723-BR-17                                           Dated: 23rd July, 2015

# Submitted To: Edivan José da Silva

Subject: Supply 1000kgs/day Flake Ice Machine With Complete Refrigeration System.

Dear Sirs,

Based on your requirement , herein , we would like to submit our best offer to you as followings. Hope it will be in line with your requirement . Any further information , please feel free to contact with us .

Looking forward to your positive response .

Sincerely yours,

Ivan Lin (Regional Manager)

FUJIAN SNOWMAN CO.,LTD

Technical Specifiaction & Price

Item     Commodities& Description            Qty.            Price

1.     Flake Ice Machine Complete ( F10A)           1 Unit          USD 5,902.00

- capacity :1000kgs/day

- installation power :4.0kw

- electrical consumption : 3.9kw

- water consumption : 0.042m³/hr

- refrigerant :R507A

- thickness of flake ice : 1.5-2.2mm

- overall dimension : 1200x735x825mm

- net weight : about 250kgs

TOTAL (FOB FUZHOU)    USD 5,902.00

TOTAL SAY    US DOLLAR FIVE THOUSAND NINE HUNDRED AND TWO ONLY

# *The price valid for one month, Quote given is on basis of exchange rate: usd=6.15rmb. It is subject to change if the exchange rate varies.

Technical data:

| 1. | 1 Set | Hermetic piston compressor unit |
| --- | --- | --- |
|  |  | Compressor Refrigerant capacity Evaporating temperature Condensing temperature Power supply Refrigerant | Copeland 6.27 -20 40 3Ph,380V,60Hz R507A | ZB38KQE-TFD kw ℃ ℃ |
| 2. | 1 Set | Flake ice evaporator (filtered fresh water) | F10S Snowkey |
|  |  | The water from external source flows into the water tank where there is a float valve for controlling interior water level. Then water is guided to the upper part of the ice machine body through the line by the pump of the water tank, charged into the water distributing pan through the water supply opening in the upper part and evenly sprinkled onto the inner wall of the evaporator by water distributing pan. The water that doesn’t freeze on the inner wall falls onto the water connecting dish, flows into the guidance trough and then into the water tank for re-circulation. Evaporator : Low-temperature carbon steel with chrome-plated Ice blade : SUS304, patented screw ice blade, lower loade,no trash ice Bearing : Industrial-purpose bearing and seal fittings Top & bottom cover : Aluminium alloy, surface anticorrosive treatment Insulation : Polyurethane foam around the drum Exterior cover : Cladded with stainless steel sheet Gear box : Good quality, stable and reliable Motor : Industrial-purpose, IP54 protection grade Water pump : Vertical-type water pump, with stainless steel blade Water tank : Stainless steel with float valve, etc. |
| 3. | 1 Set | Air cooled condensor | Greenhalgh(Australia) |
| 4. | 1 Set | Reservior (including needful accessories) |
| 5. | 1 Lot | Refrigeration valves |
|  |  | included all necessary refrigeration parts, including check valve, pressure gauge, pressure controller(high pressure, low pressure, double pressure), liquid sight glass, filter, electromagnetic valve solenoid valve and so on. |
| 6. | 1 Lot | Refrigeration pipe connecting |
|  |  | included all necessary refrigeration pipes, including gas exhaust pipe, gas return pipe, oil pipe, insulated pipe, water pipe and capillary with regulated paint. |
| 7. | 1 Lot | Compressor oil and refrigerant |
|  |  | All compressor oil and system refrigerant will be filled in the system after it is tested and accepted. (refrigerang gas is provided by the client) |
| 8. | 1 Set | Electrical box and control system |
|  |  | Including Schneider breaker and contator,Omron intermediate relay, Simens PLC,etc. |
| 9. | 1 Set | Base support frame |

# Terms and Conditions :

- Packing: export worthy package suitable for container transportation.

- Terms of payment: 30% downpayment by T/T, 70% balance before shipment by T/T

(3) Delivery time: ready for shipment within 45days after downpayment.

(4) Pre-shipment inspection :Supplier’s pre-shipment inspection is Final ;pre-shipment inspection by third Party on buyers cost.

(5) Warranty: One year after commissioning or 18 months from the date of shipment,subject to the early expiry.