Portable GPS tracker-JT600

Introduction：

JT600 is a industrial level solar portable tracker with creative power management design, which is featured in standby over 6 months, AGPS, shock-resistance , waterproof, dustproof etc.. it can be used widely in remote monitor for mobile assets, outdoor worker, government staff, explorer, people involving in outdoor sports ,elder people, kid.

Features

- Intellectual power management with standby over 6 months, supporting real time monitor to battery volume.

- Power saving ,

- Built in 3D G sensor

- Solar battery

- shock-resistance , waterproof, dustproof

- SOS lighting signal

- Storage of history data

Specification

| Type | Description |
| --- | --- |
| Function | Upload mode：TCP/UDP/SMS |
|  | Multi-working mode：Standard/Vibration/RTC |
|  | Instant SMS enquiry about current position |
|  | AGPS |
|  | Built in 3D G sensor |
|  | Real time monitor in battery volume |
|  | Solar power chargeable battery |
|  | Flashlight |
|  | SOS lighting signal |
|  | Self-Geo-fence/Geo-fence |
|  | Standby over 6 months |
|  | Serial port supported/ configuring remotely |
|  | Alarm：low battery alarm, SOS，enter/exit geo-fence |
|  | Time difference set |
|  | Alias set |
| Parameter | Size（L×W×H） | 96×51×22mm |
|  | Color | Black/Orange |
|  | Weight | 80 gram（Standard accessories included） |
|  | Working current | 60-80mA |
|  | Built-in battery | 1800mAh |
|  | Waterproof level | IP65 |
|  | Optional battery(need customization) | 2300mAh |
|  | GPS chip | Ublox |
|  | GSM | 850/900/1800/1900 Mhz |