1280II Horizontal-lift Half-tone Printing Machine

Quotation:13000USD,Fob,Ningbo

Video link: http://v.youku.com/v_show/id_XNzM0MzYzMTYw.html

Using scope：

The machine is designed for aiming at the hard distortion printing stock, the printing scope is very widely and can be used for screen printing of many plane bodies, such as paper, plastic, glass, ceramics, metal, textile and leather etc, especially for the printing of electron field PCB, soft PCB, PCB liquid state sensitization glue, SMT tin cream.

Machine Characteristics：

1、The printing head goes up and down vertically along the back main part, operated expediently and occupies little acreage. The worm reducer motor with frequency conversion driven which can ensure it goes up and down quickly and stably; High precision preload linear lead rail is used with “ITALY MEGADYNE” in-phase belt, frequency conversion timing drive the speed reducer motor, which make the whole machine more stably and credibility and can get more higher movement precision;

2、The printing table is fixed in the machine frame by support table, the distance between screen frame and table is achieved by adjusting the height of  main printing arm the stable degree is better than other model. The table surface is made of stainless steel and it’s hard to scratch and distort, and plane degree of work table is less than 0.20mm, which ensure the printing pattern much more equal and clearer;

3、The inching and lock device of the table is separately which eliminate the error caused by lock of table;

4、Two cylinders control the movement of squeegee and ink reclaim blade separately, the pressure is large and equal and can be stepless-regulatd separately which increase the service life of the half-tone and printing quality

5、The printing course control adopts the inductive switch, which can move quickly and locate on guide line, the fixation mechanism of screen frame also can be adjusted quickly, which reduce the time of exchanging frame and printing and increase the work efficiency;

6、There is snap-off device, and the height of snap-off can be adjusted, which ensure the printing precision and quality of products;

7、The run of whole machine is controlled by the PLC. The printing time and printing delay both can be adjusted and shown instantly. The speed of printing and ink returning can be adjusted quickly; There is the safe system of rising back urgently which to protect the safe of worker.

Technical Parameters:

| Model | 1280II |
| --- | --- |
| Max. printing dimension （mm） | 800*1200 |
| Max. screen frame dimension （mm） | 1100×1580 |
| Table dimension（mm） | 900×1400 |
| Max. Printing speed（t/h） | 900 |
| Overprint precision（mm） | ≤ 0.10 |
| Paper thickness（mm） | ～ 40 |
| Instant snap-off height （mm） | 0 ～ 20 |
| Power | 3P 380V 2.45KW |
| Total weight （Kg） | 900 |
| Overall dimension（mm） | 2000×1280×1700 |

Configuration list:

| No. | Name | Qty | Manufacturer | Remark |
| --- | --- | --- | --- | --- |
| 1 | PLC | 1 | Japan Omron |  |
| 2 | Inverter | 1 | Japan MITSUBISHI | Printing |
| 3 | Inverter | 1 | MITSUBISHI | Up and down |
| 4 | Exhuast | 1 | Qiangli Motor |  |
| 5 | Speed reducer | 1 | Ziguang | Printing |
| 6 | Speed reducer | 1 | Taiwan Liming | Up and down |
| 7 | Time relay | 1 | Japan Omron |  |
| 8 | Counter | 1 | Japan Omron |  |
| 9 | Hot relay | 1 | France Sehneider |  |
| 10 | AC relay | 1 | Sehneider |  |
| 11 | Micro-relay | 5 | Sehneider |  |
| 12 | Breaker | 3 | Sehneider |  |
| 13 | Press/knob button | 6 | Sehneider |  |
| 13 | Jiggle switch | 4 | Sehneider | Return up |
| 14 | Emergency stop switch | 1 | Hongbo |  |
| 15 | Small button | 6 | Hongbo |  |
| 16 | On-off power | 1 | Taiwan Mingwei |  |
| 17 | Inductive switch | 4 | H.W.L | Printing |
| 18 | Slot shape photoelectricity | 6 | Japan Omron | Up and down exhaust |
| 19 | Cylinder | 1 | Japan SMC | Snap-off |
| 20 | Cylinder | 1 | Japan SMC | Blade up |
| 21 | Cylinder | 2 | Japan SMC | Printing and ink reclaim |
| 22 | Electromagnetism | 1 | Japan SMC | Exhaust |
| 23 | Electromagnetism | 3 | Japan SMC | Printing/ink reclaim Snap–off |
| 24 | Gas and liquid changer | 1 | Japan SMC |  |
| 25 | link rod | 1 | Japan SMC |  |
| 26 | Lead rail | 2 | Taiwan ABBA | Printing |
| 27 | In-phase belt | 1 | Italy MEGADYNE |  |