Quanzhou Huaxun Machinery Making Co., LTD

Address: NO.3,Qipei Street, Gudian Community jinlong Sub-district, Licheng District, Quanzhou City, Fujian Province, China

Post code:362000

Tel ：+86-0595-22422828      Fax：+86-0595-22422727

Email:christine@papermachine.cc Skype:christine08281

TradeManager:cn1001130452  QQ:1811989902

Website：http://www.papermachine.cc  http://huaxun.en.alibaba.com/

Price Expiry Date:October 30th, 2015.

| PICTURES OF EQUIPMENT | MAIN TECHNICAL PARAMETER | UNIT PRICE(FOB price) |
| --- | --- | --- |
| HX-1575B full automatic rewinding & perforating toilet paper machine | 1.Production speed:100~200 m/min, 2.Product diameter：≦130mm; 3.Raw paper roll diameter: ≤1200mm; 4.Raw paper roll width:≤1200mm; 5.The distance between Perforated line: 100-150mm; 6. Machine power: 4.5KW (380V 50HZ, 3 phase) 7.Equipment over size (L×W×H):5.3*2.25*1.55M 8. About 4 Tons 9.Width of cutted toilet rolls: 90-120 mm 10.Requirement of Raw Paper: Double plies style is 13-20 g/m² ; Single ply style is 20-40 g/m². | USD 15，800 （with one embossing unit ,without printing） RE:USD3,500 for one color printing |
| Model HX-Z200 Full automatic Rolled Paper Cutting Machine | 1. Width of Jumbo rolls: 1500-2000 mm (Depend on the length of jumbo rolls provided by customers); 2. Diameter of jumbo rolls: φ100~φ120mm (Can be customized); 3. Production speed: Cutting 80~100 times / minute×2 rolls / time; 4. Machine power: 6.77KW（380V 50HZ） 5. Overall size of Log saw cutting assembly(L*W*H): 7080×1750×1920MM 6. Weight: About 2 tons | USD 23,000(Paper roll length:≤1800mm |
| Model HX-30 Full automatic Toilet Rolls Packaging Machine | 1.Packing specification: 4， 6， 8， 10 toilet rolls/bag or 2,4 kitchen towel rolls/bag 2. Production speed: 10-15 bags/min (8 rolls package) 3. Power supply:380V,50HZ, 3 phase 4. Power of Machine: about 5.9KW 5. Overall size of machine(L*W*H):7800 ×1600 × 1750 mm. 6. Weight of machine：About 2 tons; | USD25,000 |
| HX-ZJJ-A Paper core machine ( paper tube machine) | 1.Production Speed : 8~18m/min; 2.Core Inner Diameter:25-80mm(client can decide two sizes between this scope.) 3.Rolling Paper Layer no.:2-4 layers 4.Raw Paper Width : 70-80mm 5.Raw Paper Diameter : 700-800mm 6.Equipment Power:3.4W(380V 50HZ, 3 phase) 7.Equipment overall size(LxWxH):2800*900*1600mm 8. About 1.2T 9.Cutting length Scope:300-3000mm. | USD 7,500 |

REMARKS:

1、FOB price;

2、Warranty of the equipment：One year. The spare parts will be replaced freely by the seller within one year (exclude wearing parts). The express cost of parts should be paid by the buyer. After one year, the seller will carry on the tracking of technology and quality. The seller will provide the buyer with wearing parts which has good quality and preferential price in a long time.

3、Package：Wood Pallet and plastic film.

4、Terms of payment：it will be 30% down payment by T/T before production, then balance by T/T before the machines leave out of the seller’s company. After the seller receives all related balance, then the seller will begin to send goods to the port. The production of machine will need about 120 working days.

5. Installation and training: the seller will send technician to the buyer’s factory to install and adjust the machine if the buyer ask for this. All the expenses of the technician including two-way air tickets, accommodation(food and room), transport (bus fee, etc), and salary(salary is USD85 / day for each technician) is to be paid by the buyer. The buyer should make ready for workshop, power, raw materials in advance, then the period for the installation and adjustment and training will be totally within about 20 working days.

Some photos about packaging