SGS Series High-Speed Rotary Label printing Machine

Video link: http://v.youku.com/v_show/id_XMjI0ODA5NDk2.html

SGS type high-speed rotary trademark printing machine may be applied for printing cloth tape, cotton tape, ribbon,elastic tape, and roll paper. It may be applied for large area printing with average ink distribution, clean small prints, a-ccurate printing, and clear ink.B type rotary printing machine may print on both sides at high speed of 1 meter per second,with good printing effect and free from influence from tension of raw materials. It is the best option for printing labels and trademarks on clothes, shoes, toys, gloves, boxes and bags.

Performance advantages:

1. Connecting rod ink distributing roller can run at a high speed with average distribution.
2. With automatic oiling and transmission lubricating system, the machine has longer performance life.
3. The main electric motor takes the advantage of alternate frequency ones, offering stable currency and saving energy.
4. The electrical eye controls feeding. The machine will automatically stops if the materials are used up.
5. Printing length is counted by value input automatically. In addition, the machine is equipped with infrared ray drying system (optional).

Features:

1. High-speed full rotary printing: 3600m for each hour
2. Excellent printing effect: With round-pressing-round koster's printing, the machine can produce excellent and beautiful printing effects.
3. Simple operations, easy grasp, and convenient work
4. Wide scope of application: The machine can be applied for ribbon, tape, elastic tape, nylon tape, and roll paper.
5. Simultaneous printing on both sides: B type machine may print on both sides simultaneously.

| Model | Printing Couple | Max Printing size | Max Material Width | Printing Speed | Power | Overall Size | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SGS-1008B | Front 4 + back 4 | 95X398mm | 100mm | 60M/min | 220V/1.5Kw | cm | kg |
| SGS-1007B | Front 4 + back 3 | 95X398mm | 100mm | 60M/min | 220V/1.5Kw | 185L X 90D X 175H(cm) | 1100kg |
| SGS-1006B | Front 6 \ Front 5 + back 1 \ Front 4 + back 2 | 95X398mm | 100mm | 60M/min | 220V/1.5Kw | 180L X 90D X 168H(cm) | 960kg |
| SGS-1004B | Front 4 \ Front 3 + back 1 | 95X398mm | 100mm | 60M/min | 220V/1.5Kw | 153L X 88D X 156H(cm) | 850kg |
| SGS-1002B | Front 2 \ Front 1 + back 1 | 95X398mm | 100mm | 60M/min | 220V/0.75Kw | 132L X 85D X 148H(cm) | 550kg |